Some ideas/concepts for:
FAIR Transmission & Performance Monitoring
– first draft –
Ralph J. Steinhagen
with input from: S. Damjanovic, D. Ondreka,
S. Jüllicher, T. Radon, I. Strasik

---
Outline
- Beam Transmission Monitoring – Definition & Time-Scales
- Required tolerances	– or – “How much losses are acceptable”
  - Optimisation of particles on targets
    - “Every ion lost in the accelerator is an ion lost for physics”
    - One* of the key tuning parameters of the accelerator chain
  - ALARA – minimisation of activation and radiation permit compliance
    - How much is 'reasonable'?
  - Minimising risk of combined machine protection failures
    - Less stress on MP system ↔ more clear cut between normal and anomalous operation
- What could be achieved	– or – “why FCTs & DCCTs alone may not be sufficient”
  - proposal to include BLMs for fast in-cycle losses + radiation monitors for slow/absolute loss measurements
C. Omet's upcoming FC2WG MP talk

---
Beam Transmission Monitoring (BTM)
– Problem Definition –
transmission
beam instabilities, aperture constraints, slow beam parameter drifts
→
activation & machine protection
dynamic vacuum, ε-blow-up/tails,
slow-extraction, ...
→
cryo- & beam-halo collimators,
rad-hard magnets, extra shielding, ...
avoidable losses
(ALARA: should minimise before MP & Activation limits kick in)
less-avoidable losses
(may need to accept a given amount)
§§ Radiation Permit – limits on total dose per year (facility & external)
color white {{ dN_{collimator}(t) } over { dt }}
controlled losses
Fast current transfomer (FCT)
DC current transformer (DCCT)
DCCT
/FCT
counter
I_{source}(t) = { dN_{source}(t)} over { dt }
Ion-Source
I_{target}(t) = { dN_{target}(t) } over { dt }
Experiment
primary (secondary)
ions-on-target/s
{ dN_{loss}(t) } over { dt }
un-controlled losses
online dosimetry (abs. reference)

---
Beam Transmission Monitoring (BTM)
– Problem Definition –
transmission
Experiment
Ion-Source
primary (secondary)
ions-on-target/s
I_{source}(t) = { dN_{source}(t)} over { dt }
I_{target}(t) = { dN_{target}(t) } over { dt }
LSA
{ dN_{loss}(t) } over { dt }
Archiving
Timing
MCR
Beam Transmission Monitor
F(IFCT#1, IFCT#1, ...IDCCT#1, …) → OK? Not-OK?
…
§§ Radiation Permit – limits on total dose per year (facility & external)
controlled losses
un-controlled losses
Fast current transfomer (FCT)
DC current transformer (DCCT)
DCCT
/FCT
counter
color white {{ dN_{collimator}(t) } over { dt }}
online dosimetry (abs. reference)

---
Beam Transmission Monitoring (BTM)
– Problem Definition –
Main usage: reject (dump) beam already at low-energies & low-intensities in pre-injectors before it worsens machine operation/performance upstream
  1. online: one of the performance indicators used to tune the accelerator
  2. prevent recurring (avoidable) losses leading to unnecessary activation
  3. offline: documentation of machine performance (prediction of future runs/performance)
  4. exp. data analysis (e.g. primary → secondary RIB conversion)
  5. large losses indicative that other beam parameters may also be out of tolerance
    - e.g long. or transverse emittance blow (halo formation)
- To note: the BTM is a priori not part of the (fast) MP system, however, still needs to run reliably & continuously

---
Beam Transmission Monitoring (BTM)
– Problem Definition –
Possible BTM actions:
  - Inhibit next injection for a given beam production chain (via timing system)
    - Ideally: should be compatible with SIS18's 3 Hz 'booster mode' ↔ '<100 ms' total response time of BTM
    - KISS – Keep it Simple and Safe (with an eye on operational availability):
      - experience with by times flaky injector/source performance	→ may need to consider/keep the option of 'once doesn't count' (aka. “einmal ist keinmal”) policy for SIS18 injection (only)
      - target of '100 ms' is not a hard real-time requirement: OK if achieved with 98-99% probability & hard limit of '1 s'
        - keeps option of SW implementation open (RT Linux)
  - Inhibit extraction (via timing system):
    - option: repeat cycle
    - faster responses required: ~ < 100 ms
  - 'Fast Beam Abort'
    - probably too stringent as default ↔ (too?) tight requirement on response time and current transformer sensitivity
      - N.B. < ~1 ‰, possibly too tight based on LHC experience (easier case) & assumption: beam loss continuous after initial detection

---
Beam Transmission Monitoring (BTM)
Examples - Rules
Four transmission loss scenarios + associated rules
  1. Multi-turn injection/accumulation
    - Essentially: UNILAC → SIS18 (fast), SIS18 → SIS100 (slower)
    - Monitoring goal: '∫ IFCT-TK/HEST(t) dt' vs. 'Ifct/dcct@ start ramp'
      - easier if using <IFCT-TK(t)> but more precise using 'IFCT-TK(t)' and gating on selected injection time window
  1. Losses due to RF capture/ramp/instabilities
    - transition crossing/instabilities/space-charge
    - Monitoring goal: 'Ifct/dcct@ start ramp' vs. 'Ifct/dcct@ end ramp/before (fast) extraction'
      - probably non-issue and mainly dominated by instrument systematics
  - Fast extraction
    - Monitoring goal: 'Ifct/dcct@ end ramp' vs. 'Ifct at first location in HEST/HEBT'
      - probably non-issue and mainly dominated by instrument systematics
  - Slow extraction
    - Monitoring goal: 'Ifct/dcct@ end ramp' vs. '∫ Ifct?? dt in HEST/HEBT'
      - Monitoring tool/instrument not clear (↔ counter calibration)
p-Linac
SIS18
TK
HEBT
SIS100
pbar Target
HEBT
...
10%
10%
10%
10%
10%
10%
Global:
50%
Min,max,mean+-stdev, median,

---
Beam Transmission Monitoring (BTM)
Functional Requirements
- additional requirements:
  - Global + local trending (inj, ramp, extr): <min, max, mean ± stdev, median, ...>
    - stimulate some “healthy” BTM optimisation competition: add. traces for 'best cycle' for given beam configuration and 'worst cycle' (e.g. over last hour/day, excluding injector failures)
  - Post-processed & predictive thresholds:
    - normalised per process ('A)', 'B)', 'C)', resp. 'D)')
    - normalised per machine (BTM'A)'*BTM'B)'*BTM'C)', resp. 'D)')
    - absolute w.r.t. total particle lost (↔ activation, radiation permit)
      - predictive losses during intensity ramp-up (e.g. prevent 'low-transmission, low-intensity' → 'low-transmission, high-intensity' transition)
  - Archiving (in addition to direct logging from FCT/DCCT devices)
    - re-use common archiving system (under preparation)
    - Data retention for at least 10 years ↔ needed also from experiment/legal point of view
    - group data into one system that re-publishes the data to the timing system (interlock), MCR, archiving system, …
  - Threshold, settings, reconfigurability via LSA, …, details:
    - S. Jülicher, G. Fröhlich, “Detailed Specification of [..] 'Beam Transmission Monitor System' ” 2012-08-29, F-DS-C-12e, V3.1
p-Linac
SIS18
TK
HEBT
SIS100
pbar Target
HEBT
...
10%
10%
10%
10%
10%
10%
Global:
50%
Min,max,mean+-stdev, median,

---
Beam Transmission Monitoring (BTM)
S. Jülicher et al: Controls Specification
S. Jülicher, G. Fröhlich, “Detailed Specification of [..] 'Beam Transmission Monitor System' ” 2012-08-29, F-DS-C-12e, V3.1

---
Beam Transmission “Gretchen Frage”
“… how much losses are acceptable?”
- In a perfect world: none
- In the real world: cannot avoid certain beam losses
  - operating close to the space-charge limit
  - Touschek scattering
  - finite machine acceptance/aperture
  - finite vacuum/rest-gas interactions
  - optics errors: beta-beat, dynamic aperture, ...
  - …
- Why do we care about this now:
  - setting realistic goals, expectations and limits
    - gain experience for high-intensity operation with low-intensity beam
  - defines required accuracy, resolution and robustness of beam instrumentation
    - FCTs, DCCTs, BLMs, radiation monitors, ...
  - defines time-scales we have to act if transmission gets worse

---
Ivan Strasik @ HIC4FAIR'2015:
Tolerable Beam Losses of the Proton Beam
“uncontrolled beam losses of 1 W/m should be a reasonable limit for hands-on maintenance"
“uncontrolled beam losses of 1 W/m should be a reasonable limit for hands-on maintenance"
[Ref] N.V. Mokhov and W. Chou, The 7
[Ref] N.V. Mokhov and W. Chou, The 7th ICFA Mini-workshop on High Intensity High Brightness Hadron Beams, USA, 1999.
th
1 W/m
 6.2×10
protons/(m·s) of energy 1 GeV (uniformly distributed)
9
→
Simulation of the steel beam pipe residual activity induced by beam losses of 1 W/m
•
Simulation tool: FLUKA
•
Irradiation time: 100 days
•
Cooling time: 4 hours
Effective dose rate at 30 cm is about 1 mSv/h
possibly may need to accept 1 mSv/h due to unavoidable losses at e.g. septa, collimators, ...
However, should
not take this as a 'carte blanche' that high losses are OK	↔ ALARA principle (As Low As Reasonable Achievable)
aim at much lower global target < 0.1 mSv/h resp. < 0.1 W/m

---
Ivan Strasik @ HIC4FAIR'2015:
Beam Loss Criteria for Heavy Ions
Simulation performed by using FLUKA
Beam loss criteria: A
/A
p
i
A
– activity induced by 1 W/m of protons
p
A
– activity induced by 1 W/m of ions
i
Primary ions
(E = 1 GeV/u)
Equivalent to 1 W/m
[ions/(m·s)]
1
H
6.2
×
10
9
4
He
1.6
×
10
9
12
C
5.2
×
10
8
20
Ne
3.1
×
10
8
40
Ar
1.6
×
10
8
84
Kr
7.4
×
10
7
132
Xe
4.7
×
10
7
197
Au
3.2
×
10
7
238
U
2.6
×
10
7

---
Ivan Strasik @ HIC4FAIR'2015:
Tolerable Beam Losses in SIS100
•
SIS100 beam parameters and equivalent to 1 W/m (number of particles)
Injection
Extraction
1 W/m equivalent
1 W/m equivalent
Beam
Beam
energy
energy
(injection)
(extraction)
intensity
Protons
4 GeV
29 GeV
1.5×10
2.1×10
2×10
9
8
13
Ar
ions
1.6 GeV/u
12 GeV/u
1×10
1.3×10
1×10
40
18+
8
7
11
U
ions
1.3 GeV/u
10 GeV/u
2×10
2.5×10
1.5×10
238
92+
7
6
10
•
From the beam loss maps tolerable beam losses* (% of the beam) can be identified.
*
Collimation of protons (4 GeV)
0
10
 Halo collimators
-1
 Cryocatchers
10
 SIS100 lattice
-2
10
-3
10
-4
10
Caution: '1 W/m' is only indicative!
existing operation, shielding and radiation permit limits proton losses to <3% @ 29 GeV and nominal intensities!
→ should aim to be significantly below that limit (ALARA)
-5
10
-6
10
0
200
400
600
800
1000
s [m]
*assumes 10s proton cycle & activation limit only
*for comparison: CERN-PS: 4-8% losses achieved (data courtesy R. Steerenberg, 19th March 2012)
Caution: for protons this implies near-perfect two-stage collimation system
Beam
Loss criteria
(injection)
Loss criteria
(extraction)
Tolerable losses
(injection)
Tolerable losses
(extraction)
Protons
1 W/m
1 W/m
10 %
5 %
40
Ar
18+
ions
2 W/m
1 W/m
30 %
6 %
238
U
92+
ions
4 W/m
2 W/m
20 %
10 %
Beam losses (relative)

---
Beam Transmission & ALARA
“As-Low-As-Reasonably-Achievable” Losses – a buzz-word?
- 'golden standard': should exhaust reasonable common operation practices of controlling beam parameter known to induce particle loss (“KISS in mind” – 'actual risk mitigation' vs. 'operational availability'):
Low-intensity beams:
1. Extraction/Injection Matching
  1. first-turn trajectory steering (BPMs),
  2. energy matching (BPMs & Schottky),
  3. coarse collimation (IPMs) (removing excessive tails at low energy before propagating them to higher-energy machines)
  4. bunch-length to bucket-space matching (FCTs)
2. Closed-Orbit Cycle-to-Cycle Feedback (BPMs)
  1. aperture optimisation (coarse, circulating beam)
3. Tune & Chromaticity Correction (BPMS, BBQ)
  1. optimises space charge, ΔQ spread, dyn. aperture, beam stability
4. Emittance (blow-up) Monitoring (IPMs, FCTs)
  1. frequent cause for loss changes
High-intensity beams:
All on the left, with tighter limits, plus
1. Optics Correction
  1. Inj./extr. mismatch (Δβ, Δμ) correction (ε-blow-up optimisation)
  2. ring beta-beat correction (aperture opt. & linearises/restores symmetry of the optics → suppresses driving terms)
  3. detailed aperture optimisation (tune β bottlenecks)
2. Detailed Collimation (e.g. 2-stage for protons)
  1. see Ivan Strasik's talk @ HIC4FAIR'2015
3. Quantitative slow-extraction optimisation
  1. eval. 'Hardt condition', step-width measurement, …
4. ...
for discussion: 'acceptable losses' := losses remaining after having performed above steps

---
BTM using only FCTs & DCCTs
- May not achieve required BTM using FCTs & DCCTs alone, or would need to impose unrealistic BI design parameters
- Underlying measurement systematics
  - Coarse spacial resolution: locate losses per accelerator/transfer-line scale but only limited diagnostics where and how the particles are being lost
  - N.B. more challenging to measure pulsed RF compared to DC currents
  - permille-level resolutions can be achieved for stable beam parameters but absolute accuracy is typically limited to 1-3%, some dependencies:
    - electronic/reference-source temperature
    - EM-Interferences, cable-reflections, ...
    - RF bunch phase (FCTs, needed integration)
    - finite magnetic quantisation of ferrite core (DCCTs, weiss-domains)
    - Bunch-length (notably BMCS @ SIS100), beam position, ...
  - May improve upon some of these limitation but some are may be unreasonable below the 1% level (cost vs. reliability vs. performance → R&D, some examples)
Real-World operational problem:
  - FCT/DCCT transmission measurement accuracy limited to about 2-3%
  - ALARA (activation) transmission control aimed ideally on the sub-% level

---
Position and Time-of-Flight Dependencies
“Re-discovered” expected position dependence while doing a ±4 mm orbit bump around LHC-Pt4 (RF, BI insertion):
Usually suppressed by ±200 um orbit stability during regular operation

---
Beam Transmission Monitoring (BTM)
– Problem Definition –
transmission
Experiment
Ion-Source
primary (secondary)
ions-on-target/s
I_{source}(t) = { dN_{source}(t)} over { dt }
I_{target}(t) = { dN_{target}(t) } over { dt }
{ dN_{loss}(t) } over { dt }
beam instabilities, aperture constraints, slow beam drifts across e-septa
→
activation & machine protection
dynamic vacuum, ε-blow-up/tails,
slow-extraction, ...
→
cryo- & beam-halo collimators,
rad-hard magnets, extra shielding, ...
avoidable losses
(ALARA: should minimise before MP & Activation limits kick in)
less-avoidable losses
(may need to accept a given amount)
§§ Radiation Permit – limits on total dose per year (facility & external)
controlled losses
un-controlled losses
Fast current transfomer (FCT)
DC current transformer (DCCT)
DCCT
/FCT
counter
color white {{ dN_{collimator}(t) } over { dt }}
online dosimetry (abs. reference)

---
Beam Transmission Monitoring (BTM)
– BLMs & RadMons Extension Proposal
- Include BLMs and RadMons as complementary input1 to BTM system; operational procedure/scenarios:
- Low-intensity beams:
  - cycle-to-cycle time scale: mainly rely on FCTs & DCCTs and tune beam parameter to transmissions on 2-3%-level around established 'acceptable loss' scenario
- High-intensity beams (steps maskable by SBF):
  - use FCTs & DCCTs as for low-intensity beams
  - In addition: minimise global/localised losses using integrated BLM signals
    - N.B. qualitative not quantitative process, i.e. no hard quantitative primary-loss-to-BLM transfer function (holes in coverage, physics uncertainties, …)
    - However, some experience with BLM vs. FCT calibration at FNAL
  - On larger time-scale: cross-correlate FCT/DCCTs & BLM-based loss optimisation with absolute 'd/dt(RadMons)' reference (diagnostics/calibration to be worked out – example FNAL: ∫ Σ(BLM) dt := ∫ Σ(RadMons) dt)
1BLMs & RadMons also helps localising transmission losses and assessment w.r.t. uncontrolled and losses

---
S. Damjanovic: Energy Deposition in Coils
vs. IC-type BLM Signals
If quenching would occur, it would first be
the two innermost coils of the Sextupole/
Steerer:
maximum energy deposition
Edmax=4.5×10-13J/cm3/(lost primary)
(N.B. LHC IC-BLMs lower sensitivity threshold threshold: ~10 pA)
Idet ~ 5·104 ions/s
largest signal downstream of the cryocatcher module, at the position of BLM3
max Edep
[J/cm3/primary]
3
BLM signal [pC/primary]
BLM1
BLM2
BLM3
BLM4
BLM5
     4.5×10
-13
  2×10
-6
4×10
-5
2×10
-4
1.6×10
-4
7×10
-5
 max Pdep
[W/cm3]
BLM signal [pA]
BLM1
BLM2
BLM3
BLM4
BLM5
        1×10
-3
  3900
8×10
4
3.7×10
5
3×10
5
1.3×10
5

---
S. Damjanovic: Quench-prevention threshold for different ion beams and energies
courtesy S. Damjanovic
Quench-prevention thresholds the same for all ions/energies considered
(N.B. LHC IC-BLMs lower sensitivity threshold threshold: ~10 pA)

---
Possible BLM integration in the MCR:
CERN PS – BLM display

---
Possible BLM integration in the MCR:
FNAL example
pbar (black) & NuMi
Courtesy Bruce C. Brown, FNAL
(example FNAL: ∫ Σ(BLM) dt := ∫ Σ(RadMons) dt, details tbc.)
FNAL reference

---
Beam Transmission Monitoring (BTM)
Open Technical Questions
- Signal Sources:
  - Ring-FCTs, Ring-DCCTs + all (??) TK, HEST, HEBT FCTs?
  - Which Counters? Intensity signal from experiments (Calibration?)??
- Beam Current Normalisation (DCCTs)
  - Ideally should provide normalised currents/particle intensities
  - Performed on 'FESA front-end' or already on 'DAQ-HW'?
    - LSA function driven (settings)? (easy Day-I SW solution)
    - Dedicated SDDS? (better for HW solution)
    - Beam-based-frev generation? (good for commissioning/in case of problems)
- Total 'FCT/DCCT → BTM → Injection Inhibit' Latency
  - Is a soft real-time dead-line < 100 ms (hard limit: < 1 s) achievable by pure SW?
  - CMW subscription? Dedicated SW-Link between FCTs/DCCTs-FE and BTM?
  - Is a HW solution necessary (ala. UNILAC BTM)?
- Beam-Presence-Flag (BPF) & Setup-Beam-Flag (SBF)
  - certain BTM features are similar to BPF & SBF, however, 'SBF' is MP sensitive	(dedicated HW solution?)
  - Interface for BPF (FCT derived?) and SBF (DCCT derived?) to Fast-Abort/MP-System?

---
Beam Transmission Monitoring (BTM)
& Emittance Monitoring
... more complex subject but equally important to beam transmission control
- “Good” vs. “Bad” intensity:
  - particles outside the acceptance of up-stream accelerators
    - Mechanical and dynamic aperture!!
    - halo-particle interactions with experiment's target → background
  - prone to be lost due to or causing beam instabilities
    - “dark currents” → RF capture losses
    - abort-gap beam population → fast extraction particle across many elements
  - satellites around main bunches (inherent to BCMS) → impact on physics with bunched beam
0
1
2
3
4
5
6
7
8
9
10
7
10
8
10
9
10
10
10
11
10
12
10
13
x [sigma]
450 GeV, skew plane, bin width: 0.065 sigma, real sigma
measured data
Courtesy F. Burkart
Number of protons per bin dNp/dx
Gaussian
measured data
σ
3.6% beyond 4σ
(i.e. 10.8 x 1012 protons)
primary collimator
LHC

---
Summary
- Beam Transmission Monitoring
  - Performance: key accelerator tuning parameter & “Every ion lost in the accelerator is an ion lost for physics”
  - ALARA – minimisation of activation and radiation permit compliance
  - Minimising risk of combined failures & reducing MP stress before losses become an MP/operation issue
- Definition of 'acceptable losses – setting realistic goals, expectations and limits
  - 'In a perfect world: none' vs. 'In the real world: cannot avoid certain beam losses'
  - should keep (well) below upper limit given by facility's radiation permit and activation considerations
  - for discussion: 'golden standard of acceptable losses' := losses remaining after having applied reasonable common operation practices of controlling beam parameter known to induce particle loss:
    - Extr./inj. matching, cycle-to-cycle Orbit-FBs, Q/Q' correction, ε-blow-up monitoring → optics correction, detailed collimation, slow-extraction, ...
- Real-World operational problem:
  - 'FCT/DCCT accuracy limited to about 2-3%' vs. 'ALARA transmission control aimed ideally on the sub-% level'
    → proposal to include BLMs for fast in-cycle losses & RadMons for slow, absolute loss measurements
  - N.B. BLM thresholds to be used as relative indicators w.r.t. given setup reference
Some ToDos (dedicated task groups): CO architecture, SW/HW implementation, CSCO and BI system interfaces, ...

---
Appendix

---
Hazard and Risk for accelerators
Hazard and Risk for accelerators
Hazard: a situation that poses a level of threat to the accelerator. Hazards are dormant or potential, with only a theoretical risk of damage. Once a hazard becomes "active“: incident / accident. Consequences and possibility of an incident interact together to create RISK, can be quantified:
RISK = Consequences ∙ Probability
Related to accelerators
- Consequences of an uncontrolled beam loss
- Probability of an uncontrolled beam loss
- The higher the RISK, the more Protection is required

---
Risk Management Gradient
Poka-Yoke
'Mistake Proofing'
???
Machine Protection
intercepting common mistakes,
procedural errors, etc.
affecting machine performance
minimising machine activation
(ALARA principle)
preventing quenches
investment protection
Use-cases:
RISK
PC, FMCM (?), QPS, FCT, BLMs, ...
LSA, settings monitoring, ...
passive absorbers,
machine optic,
material choices
Devices:
Sequencer &
operational
procedures
FAIR
(SW) Interlock System
FAIR-SIS100
Fast Beam Abort Sys.
(HW Interlock System)
FAIR
Machine & System
Design
 Systems:
10s of seconds → minutes/hours
100 ms
50 us
< turn
time-scales:

---
Poka-Yoke (ポカヨケ) – 'Mistake-Proofing'
- … to avoid (yokeru) inadvertent errors (poka)
- … industrial processes designed to prevent human errors
  - Concept by Shigeo Shingo: 'Toyota Production System' (TPS, aka. 'lean' systems)
- common mistakes, procedural errors, etc. affecting machine performance
- Real-World Examples:
  - Polarity protection of electrical plugs (e.g. phone, Ethernet cable)
  - Procedures: e.g. ATM machine: need to retrieve card before money is released (↔ prevents missing card)

---
FCTs/DCCTs
Better choice as BTM for Low Energy Ion Beams
proton in H2O
courtesy PDB

---
Reconstruction Requirements I/II
Typical WCM response – Low-Frequency Base-Line
F(%omega) = int_{-infty}^{+infty} f(t) e^{- i %omega t}dt
- Naive approach: Fourier Integral definition for 'ω:=0':
- However: DC information is in-accessible:
- Intrinsic AC-coupling → requires base-line restauration
  - typ. 1rd-order zero-pole IIR filter works fine on %-level
    - Particularly important for filling patterns with many bunches (LHC: <2808)
  - observed sub-%-level drifts related bunch-filling pattern, bunch charge,...
not to scale!
Some complications at FAIR:
change of frev, bunch length & shape
SIS100: Bunch Compression & Merging Scheme (BCMS)
higher bunch harmonics (Landau)
By construction:
∫Ibunch = ∫Idroop

---
III. Base-Line Restoration – SNIP Algorithm
Example PS WCM Signal
Satellites have been deliberately produced for better proof-of-principle: