Integration Specification for the
Digitization of Analog Signals
Ralph J. Steinhagen
with input from: R. Bär, J. Fitzek, D. Ondreka

---
Digitization of Analog Signals at FAIR and SIS18 in ‘18
– Main Paradigms
traditional/old concept (underlying assumption: scopes/digitizers are expensive, RF switches are cheap)
targeted concept (underlying assumption: scopes/digitizers are cheap, RF switches are expensive)
~10 €/m
(short)
250-500 €/ch.
2-3 k€/ch.
200 -1000 €/ch.
was > 100 €/ch.
~ 200 €/ch.
~10 €/m
(long)
device #1
Front-End
(FESA, C++)
device #1
digitizer
device #2
device #2
digitizer
~ 0.5 k€/ch.
...
...
Front-End
(FESA, C++)
device #(n)
device #(n)
ethernet
~ 10 MB/s
digitizer
Front-End
(FESA, C++)
2-3 k€/ch.
device #(n+1)
Front-End
(FESA, C++)
device #(n+1)
digitizer
...
...
Controls/
Operation
device #(n+m)
Front-End
(FESA, C++)
device #(n+m)
digitizer
on-demand measurement
(selected signals, error-case, …)
con:
high-reconfiguration overhead (manual)
limited test-coverage, trending
permanent monitoring
(error-case, trending, interlocks, beam-based feedbacks, …)
Controls/
Operation
RF Switch
BLL: Brain-Locked-Loop
Not routinely connected
(only error case)
flexible
grouping option
feedbacks

---
Digitizer Integration Goals
- Primary goals
  - generic abstraction of the vendor-specific digitizer software interfaces
  - limited range of generic data post-processing on the acquired data
  - control system integration by providing standardised FESA interface
- Secondary goals
  - simplify further extensions, compactness, readability, re-usability, testability, and maintainability of the FESA implementation
  - Use of open-source signal processing and data fitting libraries
    - GNU-Radio – frame-work:	www.gnuradio.org
    - ROOT – frame-work:	https://root.cern.ch/

---
Digitization of Analog Signals at FAIR and SIS18 in ‘18
Detailed Integration Specification → in-kind contract

---
General Signal-Flow Scheme I/II
N.B. GNU-Radio inspired
Data Source
(post-) processing B.x)
Data Sink
module ID #1 + parameter set #1
channelName-ext #1
channelName
e.g. ...
module ID #2 + parameter set #2
channelName-ext #2
- Scheme can be further cascaded and combined with other modules
  - based on GNURadio‘s signal-flow concept https://www.gnuradio.org/
    - N.B. there are conceptually also other similar other projects: e.g. ADS, QUCS, Spice, LabVIEW … but with a different non-real-time (RF) signal processing
(post-) processing B.y)
Data Sink

---
General Signal-Flow
N.B. GNU-Radio inspired
signal flow-chart defined during device instantiation/start-up (tbd.)

---
From the Draft-Specification
.../b$group/1_FAIRGSI$docu/1_Machines/2.14_Common_Systems/
2.14.17_Commissioning_Control/2.14.17.1_FC2WG/Specifications/
- Two data acquisition modes:
  - A.1) Streaming-mode acquisition
  - A.2) (Rapid) block-mode acquisition
- Limited set of post-processing modules:
  - B.1) raw-measurement scaling and offset shift
  - B.2) time-base re-alignment (lag & extr. event offset compensation)
  - B.3) data aggregation and decimation (typ. to kHz → Hz)
  - B.4) real-time Short-time Fourier Transform (STFT)
  - B.5) amplitude, phase and frequency detection (I-Q demodulation)
  - B.6) χ2-type fitting and basic peak detection
  - B.7) actual versus reference comparison → interlock

---
Low-Level Acquisition Modes
A.1) Streaming-mode acquisition I/II
acquisition schematic:
user-interface (JAPC)
FESA server tasks
aggregated data
shared-memory
BP-multiplexed
BP / #1	BP / #1			...			BP / #1	BP / #2	BP / #2			...			BP / #2	BP / #3					...					BP / #3
low-level digitizer data
N.B. ~70 MS/s
timing event
user-defined
FESA server tasks/secondary RT tasks
real-time task
time
timing event
BP #1 start
timing event
BP #2 start
timing event
BP #3 start
timing system/
receiver
post-
processing
post-
processing
e.g. STFT,
actual-vs-reference
comparison,
IQ-demodulation, etc.
post-processed data
user-defined
fast (70 MS/s)
acquisition

---
Low-Level Acquisition Modes
A.1) Streaming-mode acquisition II/II

---
Low-Level Acquisition Modes
A.2) (Rapid) block-mode acquisition I/II
acquisition schematic:
low-level digitizer data
N.B. 0.5 - 1GS/s
arm
arm
arm
timing system/
receiver
time
FESA ST/secondary RT tasks
real-time task
arming event
BP #1 start
arming event
BP #2 start
timing event #3
arm
timing event
trigger #1
timing event
trigger #2
timing event
trigger #3
FESA
RT action
shared-memory
BP-multiplexed
FESA
RT action
FESA
RT action
post-
processing
user-interface (JAPC)
FESA server tasks
e.g. χ2-type fitting,
actual-vs-reference
comparison, etc.
post-processed data
post-
processing
post-
processing

---
Low-Level Acquisition Modes
A.2) (Rapid) block-mode acquisition II/II

---
General Signal-Flow Scheme

---
From the Draft-Specification
.../b$group/1_FAIRGSI$docu/1_Machines/2.14_Common_Systems/
2.14.17_Commissioning_Control/2.14.17.1_FC2WG/Specifications/
- Two data acquisition modes:
  - A.1) Streaming-mode acquisition
  - A.2) (Rapid) block-mode acquisition
- Limited set of post-processing modules:
  - B.1) raw-measurement scaling and offset shift
  - B.2) time-base re-alignment (lag & extr. event offset compensation)
  - B.3) data aggregation and decimation (typ. to kHz → Hz)
  - B.4) real-time Short-time Fourier Transform (STFT)
  - B.5) amplitude, phase and frequency detection (I-Q demodulation)
  - B.6) χ2-type fitting and basic peak detection
  - B.7) actual versus reference comparison → interlock

---
Module B.1)
raw-measurement scaling and offset shift
nomen est omen:
y_{"meas"} = a_{"cal"} cdot y_{ ADC } "[ V ]" ~+~ y_{ "offset" }
- aim: acal relating low-level digitizer voltage measurement to physical device property (e.g. kV kicker voltage, RF gap-voltage, ...)
- calibration factor acal and offset option, either
  - multiplexed ↔ (possibly) different for each beam processes & beam-production chains
  - non-multiplexed ↔ constant for all beam processes & beam-production chains

---
Module B.2) time-base re-alignment
Lag & extraction event offset compensation
- Correction for the actual extraction event (see Bunch To Bucket Transfer System1)
  - Digitizer-Step 1: acquire ‘tmeas>10 ms + 10k samples’ with extraction timing event t0
  - Digitizer-Step 2: wait for timing meta-information informing about actual text (low-level mechanism tbc.)
  - Digitizer-Step 3: shift and crop data by t = text - t0
t0
text
1Technical Concept of the FAIR Bunch To Bucket Transfer System (F-TC-C-05e), https://edms.cern.ch/document/1514162/6

---
Module B.3)
Data Aggregation and Decimation
- Digitizer Streaming to FECs
  - min/max value over the last N values
  - simple decimation or arithmetic mean μ of the last N values
- FEC-based Low-Pass Filter and Decimation
  - IR-based band- or low-pass filter (GNU Radio)
- Band-Pass Filtering and Down-Conversion
  - GNU Radio: ‘Frequency Xlating FIR Filter’:

---
Module B.4)
Real-time Short-time Fourier Transform (STFT)
  - with xn being the n-th sample of the input, wn one of the user-selectable windowing function (e.g. Hamming, Hann, Blackman, Rectangular, Kaiser), m the acquisition length in terms of samples, fi in [fmin, fmax] for which the frequency component in the signal should be evaluated, and nf the frequency binning (N.B. k = 0 ... nf).
Noteworthy choices, ...
1. whether fk ↔
  1. sampling clock fs → standard spectrum analyser functionality → further norm. needed
  2. revolution frequency frev → normalised spectrum → e.g. direct Δp/p or ΔE/E measurement
2. on fmin & fmax whether to compute spectrum1
  1. full spectrum (DC → fmax = fs/2 or frev/2), or
  2. subset of spectrum (e.g. n-th harmonic of frev → fk in [(n-1)frev, (n+1)frev]), or
3. on frequency binning Δf (normally Δf ≥ 1/Tacq)
- Examples on next slide
STFT left lbrace [x] right rbrace ( m, f_k) := Sum from { n= - m/2 } to {n= + m/2} x_n cdot w_n cdot e^{i 2 %pi f_k } ~~"and"~~ f_k = f_{min} + k cdot %DELTA f = f_{min} + k cdot { {f_{max} - f_{min}} over {n_f} }
1 N.B. fmin = 0, fmax = fs/2 & Δf =1/m implies FFT implementation, DFT or Goertzel algorithm otherwise

---
Module B.4) Short-time Fourier Transform
Older example: BBQ @ CERN-PSB, frev ≈ 2 MHz
3.
4.
2.
1.

---
Module B.5)
Amplitude, Phase and Frequency Detection
- Main application:
  - Ring-RF Cavity monitoring, actual-to-reference comparison → interlock
e.g. RF gap voltage
e.g. group-DDS
reference

---
Module B.6)
a) χ2-type fitting and basic peak detection
%chi^2 = Sum from { i=0 } to { N } left({y_i - f(x_i)} over {%sigma_i} right )^2
  1. Generic Chi-square based fitting (ROOT-based):
G := { %chi^2 } over { n_p }
%DELTA G = abs { G - 1 }
- Function representation (type: string): ROOT allows a wide range of string-based function description (see class documentation for ‘TFormula’ for reference1), some examples include, e.g.
  - ‘gaus’ for a simple fit of a Gaussian function,
  - ‘sin(x)/x’
  - ‘[0]*sin(x) + [1]*exp(-[2]*x)’
  - ‘x + y**2’
  - ‘gaus + pol0(3) + expo(4)’, ‘gaus+(x>30 && x<90)*pol2(3)’, or
  - ‘(x<[0]?0:1*[1])’ for fitting the time offset and amplitude of a Heaviside step function.
see1: https://root.cern.ch/doc/master/classTFormula.html

---
Module B.6)
b) Basic Chi-square-based Fitting
  1. Generic Chi-square based fitting (ROOT-based)
  2. Fitting of spectral peaks:
[1] R.J. Steinhagen, M. Gasior, and S. Jackson, “Advancements in the Base-Band-Tune and Chromaticity [..]”, Proceedings of DIPAC2011
[2] R.J. Steinhagen, “Tune and Chromaticity Diagnostics”, CAS, Dourdan, France, 2008, pp.317

---
Module B.6)
χ2-type fitting and basic peak detection
… based on operational experience at CERN and similar systems, the following post-processing algorithm shall be implemented1,2:
1. calculate the raw-spectra Sraw(f) based on the n-sample oscillations data,
2. compute (averaged) magnitude spectra |Sraw(f)|,
3. apply a nmed-wide median-filter → |Smed(f)|,
4. apply a ±nlp-wide sliding average-filter → |Slp(f)|,
5. find highest peak Qest. in |Slp(f)| within the given
6. boundaries Qest. ∈ [fmin, fmax],
7. find highest peak Qraw in |Sraw(f)| around the previous 'Qest.·n/2 ± nmed/2' estimate,
8. refine the binning-limited Qraw estimate by fitting the tune resonance to a Gaussian distribution.
9. compute the full-width-half-maximum estimate at the peak, and compute the Gaussian-equivalent width as:
%sigma approx {"FWHM"} over { 2sqrt{2ln2} }
[1] R.J. Steinhagen, M. Gasior, and S. Jackson, “Advancements in the Base-Band-Tune and Chromaticity [..]”, Proceedings of DIPAC2011
[2] R.J. Steinhagen, “Tune and Chromaticity Diagnostics”, CAS, Dourdan, France, 2008, pp.317

---
From the Draft-Specification
.../b$group/1_FAIRGSI$docu/1_Machines/2.14_Common_Systems/
2.14.17_Commissioning_Control/2.14.17.1_FC2WG/Specifications/
- Two data acquisition modes:
  - A.1) Streaming-mode acquisition
  - A.2) (Rapid) block-mode acquisition
- Limited set of post-processing modules:
  - B.1) raw-measurement scaling and offset shift
  - B.2) time-base re-alignment (lag & extr. event offset compensation)
  - B.3) data aggregation and decimation (typ. to kHz → Hz)
  - B.4) real-time Short-time Fourier Transform (STFT)
  - B.5) amplitude, phase and frequency detection (I-Q demodulation)
  - B.6) χ2-type fitting and basic peak detection
  - B.7) actual versus reference comparison → interlock

---
General Signal-Flow

---
Conclusions
- Main focus: generic acquisition and common post-processing of analog signals in the range of a few MHz to hundreds of MHz (in theory: also > GHz)
  - vendo-specificr HW abstraction (→ future upgrades of newer version or different models)
  - two basic low-level acquisition modes: continuous & rapid block-mode
  - set of 6 post-processing modules
  - maintainability & testability (unit testing, testing, testing, ...)
- Next steps:
  - (informal) ‘Engineering Check’ via FC2WG (& in-kind partner), main aim:
    - identify important missing features
    - identify important conceptual errors or consistency errors
  - formal ‘Engineering Check’ via EDMS (↔ collection of signatures of those who gave feedback)
  - formal ‘EDMS Approval’ (↔ collection of signatures)
- Open Items (N.B. not just digitizer, but also BPMs, BBQ, ...):
  - handling of 3D-data structures in FESA: Japc, Archiving, …
    - ???
  - generic handling of (N>3)-dim data structures
    - staged not for 2018
  - transmission of extraction event meta-information (via timing message, data-supply, … ?)
    - staged not for 2018
  - ‘Form’ over ‘Performance’, but should define a minimum standard and practical upper-boundary (engineering margin)
    - parallelisms, FEC platform, ...
  - ...