2018-09-05 FC2WG Meeting #33
Digitizer Status Update &
SDR System & Integration Options
https://edms.cern.ch/document/1823376
R. J. Steinhagen
with input from: R. Bär, C. Handel, J. Fitzek, D. Ondreka, V. Sanjari, A. Schwinn

---
Scope
- FAIR and notably the FAIR Control Centre will deploy a ‘fully-digitial’ control paradigm:
  - automatic monitoring
    - performance tracking & early fault detection
    - quantitative/semi-automatic feedback and setup applications
  - assisted isolation of HW faults (‘ref-actual’-monitoring)
  - remote expert diagnostics (as needed)
  - also: pre-requisite prior to major ‘alt-HKR’ upgrades and/or move of operations to FCC
- Primary goals
  - generic abstraction of the vendor-specific digitizer software interfaces
    - explicitly open for new/future vendor/digitizer models extensions
  - limited range of generic user-definable data post-processing on the acquired data
  - control system integration by providing standardised FESA interface
- Secondary goals
  - simplify further extensions, compactness, readability, re-usability, testability, and maintainability of the FESA implementation
  - Use of open-source signal processing and data fitting libraries
    - GNU-Radio – frame-work:	https://www.gnuradio.org
    - ROOT – frame-work:	https://root.cern.ch
- Not a new concept, existing specifications:
  - “Soft Oscilloscope System” https://edms.cern.ch/document/1176042/3
  - “Digitization of Analog Signals in the FAIR Accelerator Complex” https://edms.cern.ch/document/1823376/
ongoing..

---
Digitization of Analog Signals at FAIR I/II
https://edms.cern.ch/document/1823376/
traditional/old concept (underlying assumption: scopes/digitizers are expensive, RF switches are cheap)
targeted concept (underlying assumption: scopes/digitizers are cheap, RF switches are expensive)
~10 €/m
(short)
250-500 €/ch.
2-3 k€/ch.
200 -1000 €/ch.
~ 200 €/ch.
~10 €/m
(long)
device #1
Front-End
(FESA, C++)
device #1
digitizer
device #2
device #2
digitizer
~ 0.5 k€/ch.
...
...
Front-End
(FESA, C++)
device #(n)
device #(n)
ethernet
~ 10 MB/s
digitizer
Front-End
(FESA, C++)
2-3 k€/ch.
device #(n+1)
Front-End
(FESA, C++)
device #(n+1)
digitizer
...
...
Controls/
Operation
device #(n+m)
Front-End
(FESA, C++)
device #(n+m)
digitizer
start deployment ≥2018 (SIS18), crucial for:
migration to new FAIR Control Centre (FCC),
optimisation of commissioning & operation
tracking/isolation of faults (↔ post-mortem)
less-biased performance indicator
link: more details
on-demand measurement
(selected signals, error-case, …)
con:
high-reconfiguration overhead (manual)
limited test-coverage, trending
permanent monitoring
(error-case, trending, interlocks, beam-based feedbacks, …)
Controls/
Operation
RF Switch
BLL: Brain-Locked-Loop
Not routinely connected
(only error case)
flexible
grouping option
feedbacks

---
Digitization of Analog Signals at FAIR II/II
https://edms.cern.ch/document/1823376/
GNU Radio
eliminated/simplified by new FESA rewrite/upgrade

---
General Signal-Flow Scheme
N.B. GNU-Radio real-time streaming processing inspired
Data Source
(post-) processing B.x)
Data Sink
module ID #1 + parameter set #1
channelName-ext #1
channelName
e.g. ...
module ID #2 + parameter set #2
channelName-ext #2
- Scheme can be further cascaded and combined with other modules
  - based on GNURadio‘s signal-flow concept https://www.gnuradio.org/
    - N.B. there are conceptually also other similar other projects: e.g. ADS, QUCS, Spice, LabVIEW … but with a different non-real-time (RF) signal processing
(post-) processing B.y)
Data Sink

---
General Signal-Flow Scheme
Simple Example – AEG Dipole Acquisition
Optional (for non-FESA use):
GUIs↔ usefull for prototyping
(ignored when using FESA)
Cascade Sink (+ time‑domain & frequency domain sink)
communication with FESA
groups common data aggregation/reduction (n MHz → 10 kHz → 1kHz → 1 Hz
+ STFT frequency spectrum (8192 bins@finput) updated at 1 kHz for full cycle
+ default triggered DAQ
N.B. a bit of scientific rigour: measurement always includes value and it’s error propagation, i.e. <x> ± σrms

---
Short-Term-FFT, Goertzel-Transform etc.
Example I/II

---
Short-Term-FFT, Goertzel-Transform etc.
Example II/II

---
RF-Amplitude, Phase, and Frequency Detection
Example I/II

---
RF-Amplitude, Phase, and Frequency Detection
Example II/II

---
Generic Chi-square based fitting
Example
1st order slope
step-response

---
Low-Level Acquisition Modes
A.1) Streaming-mode acquisition I/II
acquisition schematic:
Sequence data
BPs
BP / #1	BP / #1			...			BP / #1	BP / #2	BP / #2			...			BP / #2	BP / #3					...					BP / #3
low-level digitizer data
N.B. ~125 MS/s
cont. streaming
~ 5 GS/s bursts
FESA server tasks/secondary RT tasks
real-time task/BPM FPGA
time
timing event
BP #1 start
timing event
BP #2 start
timing event
BP #3 start
timing system/
receiver
user-interface (JAPC)
FESA server tasks
x WR event
x WR event
e.g. instant orbit,
closed orbit@ < 1 kHz,
...
triggered data
timing event
user-defined
user-defined
fast (… 5 GS/s) acquisition
eliminated/simplified by new FESA rewrite/upgrade

---
Generic Acquisitions I/II
Specified FESA Data Streams
Following modes of acquisition would be expected to be served simultaneously (though some of them could be implemented as down-sampled copies of the higher bandwidth acquisition):
1. Slow-acquisition (FESA property: ‘Acquisition’) – sub-choices (selected via CMW-filter):
  1. 'Sequence' acquisition between ‘beam injection’ and ‘beam extraction’: the specific signal averaged and decimated to the rate needed for the given client (e.g. 1 kHz). → property notifies complete trace as a function of time at the end of the sequence (up to 30-60 s)
  2. ‘Continuous’ real-time data publication during the cycle (↔N.B long SIS100 cycles and/or storage rings): → property notifies single measurement at typical update rate around 10-25 Hz
    1. use-case: user-level applications (inj./extr. steering), software-based real-time feedbacks, ...
  3. ‘Instant’ signal acquisition: → property notifies single measurement at pre-defined time delays (ms-scale)
    1. software interlock on injection/extraction orbit deviations (via MASP)
2. Fast block-mode acquisition (also ‘Acquisition’):
    - up to 10 external user-defined timing triggers per sequence (ie. each injection, extraction etc.)
      - corresponding CMW property subscription: e.g. ‘TRIGGERED’ or name of specific timing event
    - horizontal channel settings are assumed to be fixed per digitizer
Post-Mortem (FESA property 'PostMortem'): not finalized but provisionally:
  1. first circular buffer storing each signals @ 1 kHz for the last second of beam or full cycle
  2. second circular buffer storing the last 1k (10k?) turns at maximum sampling rate

---
Data Acquisition, Client Interfaces & Synchronisation
similar to/the same as
BPM, Trafo, BTM, handling
indiv. HEBT-in trajectories
published per injection
time (not to scale)
Circular Machine Cycle
e.g. SIS100, CR, HESR, CRYRING, SIS18, ESR
transfer line 1
e.g. SIS18 → HEBT → SIS100
or: SIS18 → HEBT → ESR
or: ESR → HEBT → CRYRING
transfer line 2
e.g. SIS100 → HEBT → p-target/CR
or. SIS100 → HEBT → CBM
beam/batch intensity [ppb]
HEBT rigidity
beam rigidity
FAIR Timing:
timing: prepare
timing: start ramp
or tn+1
timing: injection t1
timing: end ramp
 or tn+2
timing: extraction
('beam-out')
 or tn+3
timing:
Merging/rotation #2
timing:
merging/rotation #1
timing: injection t2
timing: injection t4
timing: start segment
('beam-in', t:=0)
orbit acquisition @ 1 kHz (100 Hz, 10 Hz, 1 Hz, N.B. batch average)
1st
2nd
3rd
4th batch
extracted beam (slow)
indiv. HEBT-out trajectories
published per extraction
extracted beam (fast)
trajectory acquisition

---
FESA Acquisition(Sepctra) Property Layout
GUI in preparation
acquisition mode:
STREAMING
FULL SEQUENCE
SNAPSHOT
POST_MORTEM
TRIGGERED
signal name, e.g. ‘GSI11MU2:I_Circuit@1kHz’
WR event (optional), e.g. ‘CMD_BEAM_INJECTION’, ‘CMD_BEAM_EXTRACTION’, ‘CMD_START_ENERGY_RAMP’, ‘CMD_CUSTOM_DIAG_[1,3]’
user data:
acqTriggerStamp (UTC-seconds of trigger/start)
channelTimeBase (N.B. time stamps relative w.r.t. 1st injection)
channel[Actual/User]Delay ( ↔ bunch-to-bucket-inj./group delay)
channelName
channelValue (N.B. array)
channelError (N.B. array)
channelUnit
[..]

---
Digitisation of Analog Signals
Next Steps
- Sub-categories:
  - a) time-domain: functional actual-vs-reference monitoring (DC – up to 2GHz)
  - b) frequency-domain: SA- & VNA-type funct. Δfbw≈20 MHz@fLO≈DC…6 GHz
  - c) video-signal (IPM, screens, etc.) → not covered
    - existing BI technology/integration, main issue: budget/MC commitment
    - need interim solution for ‘alt-HKR’ retrofitting → personell resources needed
  - d) generic signals < 1 MHz bandwidth → also not covered (e.g. QPS, BI)
    - different strategy: local low-cost high-ADC-density controller, ...
- Frequency-domain covering Software-Defined-Radio (SDR)-like functionalities:
  - e.g. RF vector signal analyzer, RF network analyzer, RF signal generator, ...
    - DAQ of Rx-path is very similar to existing time-domain digitizers
      - N.B. often already existing GNU Radio integration + (tbd.) integration of White-Rabbit-Trigger/Synchronisation integration
    - Open-question:
      1. SDR hardware choice (next slide)
      2. Integration of Tx-path: signal/function types, triggering schemes
      3. Low-level RF feedback functionalities
                  - probably requires (custom) FPGA modifications (functionality needed)
< 30 MHz ↔ time-domain digitizer
> 30 MHz → proper SDR

---
Software Defined Radio
Wikipedia: “[..] components that have been traditionally implemented in hardware (e.g. mixers, filters, amplifiers, modulators/demodulators, detectors, etc.) are instead implemented by means of software on a personal computer or embedded system. [..]”

---
Software-defined Radio
Hardware choices – Impressions
- wide range of academic, commercial, and military applications:
  - cellular radios (3G, 4G, 5G), (passive) radar systems, SIGINT, …
  - market at its infancy and will likely continue to grow significantly
- focused on commercial/open-source systems → easier integration (GNU Radio, less NDAs, …)

---
Software-defined Radio
Market Survey & Pre-Selection
high-end
low-
end

---
Most SDRs already integrated in GNU-Radio (via UHD)
N.B. still requires WR event/synchronisation (via GPIO? Rx?)
here:
simple FM receiver

---
Known/possible SDR Applications@FAIR
- SIS18/SIS100 K.O. exciter monitoring/signal generation:
  - broad-band signal surveillance (+ time-domain digitizer)
  - flexible spectrum & time dependencies for excitation
  - option: fast(er) spill-extraction FB?
- Generic accelerator-related diagnostics
  - Long. Schottky: momentum width, energy mismatch, intensity, ...
  - trans. Schottky: Q/Q’, emittances, … ??
  - experiments: use-cases see V. Sanjari’s presentation
- RF leakage monitoring/EMC compliance for UNILAC RF driver (pLinac?) ??
  - N.B. 36.136 MHz ↔ (civ/mil: BOS, micros, ...)
  - N.B. 108.408 MHz ↔(civ/mil: aviation, navigation, ...)
- Low-Level RF (reuse same HW/SW platform)?
  - second-/third-order harmonic measurements
- <you application here> – it’s a generic CO platform that can be further expanded:
  - under the responsibility of CO:
    - Digitizer (SDR) HW integration
    - HW abstraction/driver-integration (GNU Radio)
    - basic signal post-processing & FESA export
  - Under the user responsibility
    - RF analog input adaptation & cabling (ie. AFE, analog front-end)
    - non-standard signal post-processing, i.e. custom FPGA processing/modifications

---
Integration of Tx-path I/II
– excitation types (+ WR triggered → needs proof-of-concept)
- No excitation/white or remnant noise
- Kick/frequency sweep aka. ‘chirp’
  - enableExcitationTx-[A,B]
  - exAmplitude[A,B]
  - chirpStartDelay t0, chirpStopDelay t1
  - chirpStartFreq[A,B] f0, chirpStopFreq[A,B] f1
  - + all the above as function of time in cycle/BPC sequence
- Phase-Locked-Loop (PLL) System
  - Similar to chirp but on slower time-scales
  - Beam-Transfer-Function (BTF)
- Bandwidth-limited/shaped white-noise
  - Uniform, Gaussian,Laplacian, Impulse, inverted-Gaussian, ...
  - + all the above as function of time in cycle/BPC sequence
exAmplitude[A,B]
t0, f0
t1, f1
time
amplitude

---
Integration of Tx-path II/II
– excitation types (+ WR triggered → needs proof-of-concept)
- Deterministic signal source
  - sine, square, triangle, saw-tooth, sin(x)/x, gaussian, half-sine
- Arbitrary Waveform Generator (SDR can operate as DDS generator)
  - options are limitless but ressources to implement these are finite → need to prioritise
- External Rx-driven output relation (ie. FB-loop, required FPGA mod)
  - simple PID +simple Smith-Predictor for 1st/2nd-order latency compensation
- Misc:
  - ADC/DAC clockSource = external vs. internal oscillator
  - FirDecimationValue, ...
  - external gating???

---
Digitizer Status Summary
& SDR Open Questions
- FAIR Control Centre (FCC): ‘fully-digitial’ control paradigm
  - pre-requisite prior to ‘alt-HKR’ to FCC move
  - automatic monitoring, performance tracking & early fault detection
  - assisted isolation of HW faults (‘ref-actual’-monitoring) & remote expert diagnostics (as needed)
- Primary goals of digitizer integration:
  - generic abstraction of the vendor-specific digitizer software interfaces (via GNU Radio)
  - limited range of generic user-configurable data post-processing on the acquired data
  - control system integration by providing standardised FESA interfaces
- Sub-categories:
  - time-domain: functional actual-vs-reference monitoring (DC – up to 2GHz)
  - frequency-domain: SA- & VNA-type funct. Δfbw≈20 MHz@fLO ≈DC…6 GHz
  - video-signal (IPM, screens, etc.) → not covered (existing BI technology/integration)
- Open-question regarding frequency-domain digitization via Software-Defined-Radios (SDRs):
  - SDR hardware choice → cross-check favoured candiates
  - Integration of Tx-path: signal/function types, triggering schemes
    - to be demonstrated: integration of White-Rabbit-Trigger/Synchronisation integration (via GPIO?)
  - Low-level RF feedback functionalities → … an option to be followed-up?
ongoing..
< 30 MHz ↔ time-domain digitizer
> 30 MHz → proper SDR

---
Appendix

---
Final Vendor/Model Selection
PicoScopes from Pico Technology
- Low-Bandwidths (< 20 MHz)
  - PicoScope 4824, 7 (8) channels, 11.3 ENOB @ 20 MHz)
    - N.B. ~ 16 ENOB @ 10 kHz (ΔI/Imax ~ 10-5)
  - 2018: primarily used for EPC-related systems (→ 2018: “AEG”)
    - planned to digitize: Iref, Uref, Iactual, Uactual, ΔI, Uint, + 1 spare
    - 8th channel for WR timing synchronisation
- Medium-range Bandwidths (< 200 MHz)
  - PicoScope 3403D MSO ↔ 3406D MSO), 4 ch, 6.9 ENOB @ 200 MHz
    - N.B. ~ 7.9 (15) ENOB @ 10 MHz (10 kHz) (ΔU/Umax ~ 10-3 (3·10-5))
  - 15 (16) digital channels → triggering e.g. on fast RF loops states, etc.
  - 2018: primarily for Ring-RF (→ “Gap Voltage”) and HV-extraction kicker trigger acquisition
- High-Bandwidth (< 500 MHz, (1 GHz))
  - PicoScope 6402C↔ 6404C, 4 channel, 7.3 (7.9) ENOB @ 500 (200) MHz
  - 2018: primarily used for HV extraction and tune kicker waveform
- Open: specification for further digitizer devices
  - tentatively: Ettus Research SDR for spectra-related applications
N.B. Ordered/deploy 150+ digitizer for 2018/19 for SIS1/ESR/Cryring

---
Signal Flow-Graph → SAT I/II

---
Signal Flow-Graph → SAT II/II