FCC – FAIR Control Centre
Existing Infrastructure, functional User-Requirements, Ergonomics & Next Steps
Ralph J. Steinhagen for the FC2WG & FCC-WG, based on previous work and input from: Ch. Arzinger-Mayer, K. Berkl, J. Lindenberg, A. Fischer, P. Spiller, R. Bär, C. Omet, D. Ondreka, S. Reimann (deputy), U. Scheeler, P. Schütt, G. Stephan (CE), M. Schwickert
special thanks: R. Giachino, M. Lamont, D. Manglunki, R. Steerenberg (CERN)
Extract from Campus-Masterplan 09/ 2016

---
Outline I/II
- Discontinued 17.1 MCR option: issues w.r.t. accessibility, being a controlled area, ... (ECR in 2015)
- New control room and additional support infrastructure needed for FAIR
  - Existing GSI “alt-HKR” is
    1. too small for an effective commissioning & operation, and
      - need long-term ~25 ‘workstations‘ (8+ accelerators, ↔ > 600 m2)
    1. not adapted to new FAIR control & OP paradigms
      - analog signals (manual labour-intensive operation), unsafe/unsustainable w.r.t. machine protection and high‑intensity operation
  - Single common platform for more efficient accelerator operation, communication across different domains, ... → improved facility performance (i.e. no multitude of local control rooms)
  - Positive public portrayal of GSI & FAIR: core facility/experiments in-accessible to public and most scientific visitors → FCC being the ‘heart’ & ‘brain’ of the facility
- Abstracted previous site-specific concepts → generic FCC user-requirements → became input to Campus Master Plan (CMP)
  - mainly site/building parameters/recommendations: location, outer hull and additional infrastructure, also “HKR” → “FAIR Control Centre (FCC)”
- FAIR Management reviewed CMP in 2016: confirmed FCC prioritisation within CMP, decided for ‘new building’ option, and to continue detailed & expedient planning targeting a soon-as-reasonable-achievable realisation

---
Outline II/II
- Today: presentation of accelerator operation related FCC user‑requirements (80% of the input to CMP)
  - update involved present and future stake-holders on current state
  - link to ‘FAIR Accelerator Control and Operation‘ concept (dealt by FC2WG)
  - basis for further in-depth detailing of user-requirements in view of tendering process
- Next Steps via FCC Project-Group (smaller circle, interest-based representation/mandate)
  - Elaborate missing requirements from other groups tightly intertwined with accelerator: Cryo, TI, (accelerator-kin) experiments, ... → remaining 20% of input to CMP
- Two new aspects since 2016:
  - office spaces above main control room: collection of user-requirements, development of usage concept, ...
  - main control room planning combined/advanced with primary building tranche → FCC user-requirements need to be finalised by March ‘17 to minimise overall planning costs and potential additional post-award contract charges afterwards

---
Existing Infrastructure:
'GSI Hauptkontrollraum (HKR)'

---
Existing Infrastructure:
GSI “alt-HKR” floor plan (328 m2)
7.2 m
7.2 m

---
HKR – heute
Aufteilung Konsolen
Existing Infrastructure:
GSI HKR consoles
8% LEBT / MEBT / HEBT
Arbeitsplätze Quellen unzu-sammenhängend
Konsolen sehr tief für Oszi + Röhren (teilw. obsolet)
“Analog Betrieb“...
Kopierer
ESR
UNILAC
SIS 18
MEBT
HEBT
OLOG
RGM
LEBT
Quellen
Entwicklung
3 x Drucker
ZKS
Entwick-lung
Maschinen-Entwicklung/SD
Farbcodes:
Quelle
Beschleuniger
Speicherring
Experiment
UHV
Quelle
ESR
Experi-ment
courtesy C. Omet
OLOG
HITRAP
Plaketten 3 x Drucker

---
HKR – heute
Aufteilung Flächen
Existing Infrastructure:
division of ground surface area
328 m² Grundfläche
200 m² Nutzfläche
41% für Konsolen, Bedienflächen
39% für Wege
14% „tote“ Flächen für Wartung
6% für Sitzecke, etc.
60% eff. Nutzfläche
courtesy C. Omet

---
Struktur FAIR
GSI x 2 (2,3)
Migration Strategy
GSI 3 → FAIR 8½ (11+) accelerator(-like) machines
p-Linac
SIS 18
SIS100
SIS 300
UNILAC
EH
EX
FRS
APPA
p-bar
SFRS
CBM
existing:
3 Ion-Sources
1 LINAC
1 synchrotron + 1 storage ring
13/7 transfer-lines (MEBT / HEBT)
3 experimental areas
ESR
CR
NESR
Cry-
Ring
HESR
(PANDA)
FLAIR
new:
1 proton source + linac
4 synchrotrons & storage rings
18 (26) transfer-lines
4 (5) experimental areas
MSV 0-3
MSV 4-6

---
for comparison: BNL Accelerator Complex
(excluding ATF etc. R&D)
LINAC
BOOSTER
AGS
TANDEMS
RHIC
EH
EX
G-2B
NSLS-II
similar number of accelerators to FAIR, but
lower complexity (shorter chains)
quasi-static operation (infrequent ion-type changes per year)

---
for comparison: FNL Accelerator Complex
Booster
Main
Injector
Linac
EX
p-bar
Tevatron
Accumulator
Debuncher
EX
similar complexity/number of accelerators, but
quasi-static operation & primarily (anti-)protons only

---
for comparison: CERN Accelerator Complex
N.B. CERN-OP
crew + support:
 ~ 90+20 FTEs
p-Linac
BOOSTER
(x4)
PS
LINAC4
Isolde
EX
EastArea
p-bar
n-ToF
REX++
SPS
AD
EX
North
Area
LEIR
LINAC3
ELENA
LHC
CNGS
AWAKE
HiRadMat
similar complexity/number of accelerators, but
semi-static operation (mode of operation change typically ~ weeks → months)

---
Global Requirements & Operational Constraints
1. Much larger facility, cannot reliably extrapolate from present 'UNILAC→SIS18→ESR' operation to requirements for FAIR (3 → 9+ accelerator(‑like) structures)
2. Will be in a constant flux of frequent adaptations to new cycles/beam parameters, etc. present estimate:
  - avg. experiment run: ~ 1-2 weeks per exp. + many new storage rings and transfer lines with high(er) complexity → machine setup time-scale
    - increased number of users & parallel operation
    - added complexity: long accelerator daisy chains O(n5)
    - present efficiency for physics εUNILAC+SIS18 ~ up to 75% → >90% (target, see appendix)
  - high-intensity operation requires more and better fine-tuning
    - dynamic vacuum, machine protection & activation, collective effects
  - limited operator resources: 4-5 (beam operation) + 1 (infrastructure, cryo)
→ need to be smart and develop efficient commissioning procedures, training and tools to facilitate fast turn-around and to maintain/improve present operational performance
→ control and operation aspects are reflected in FCC design/user-requirements

---
FAIR Control Centre & Operation
Concept Development
– User Community Organisation
Campus Development
(G. Stephan)
Experiments
(fixed-target- & accelerator-based)
FAIR Control Centre
(planned: 25 workstations)
Equipment
Groups
(GSI: ~28 on-call experts → FAIR: ??)
Skeleton crew:
  5 accelerator operators (& 1 shift leader)
  1-2 cryo-operators
  1 TI operator (tbc.)
additional:
  ~5 machine/system experts
  ~5-10 physicists from accelerator-based experiments
Machine Coordinators
4 on call machine experts
UNILAC, SIS18/100, ESR, FRS
System Design
Technical Infrastructure (GA)
(cooling, ventilation, )
OP Coordinator
Visitors
(150-200/day)
(I. Peter et al.)
FAIR Management

---
FCC ... more than a 'Main Control-Room'
additional required facilities
Equip. group offices
& laboratories/workshops
new:
Offices
(generic, w/o labs)
Main Control Room
(25 work stations*, ≥600 m2,
< 35 dB(A) ambient noise, fully digital
open communication lines,
> 3 (5) m ceiling, false floor, ...)
OP ready
room
toilet
crisis
response
centre
shower
Conference Room
(25 + 25 persons)
see Appendix for detailed functional user‑requirements that went into the CMP
kitchen/
ready room
Visitor Gallery
(25 p. → n qm,
slightly elevated)
Small Meeting
Room (12p)
< 2 min./100 m
FCC - FAIR Control Centre
gross surface: ~ 1000 m2
< 5 min.

---
Open Communication Line of Sight
here: old MCR-in-Canteen proof-of-concept
‘No pillars user-requirement’:
impedes line-of sight
less efficient eye-to-eye com.
visibility of shared fixed-displays
Non-ideal visitor’s view
limits console layout/future
upgrade options
“‘room‘ must not get in the way of the primary purpose of the room“

---
25 workstations → > 600 m2 surface
FCC ceiling design reference height: 5 m
The 5m ceiling height avoids the “parking house effect” and is also beneficial for the acoustics, ventilation system, indirect lighting and fixed-display concept
Courtesy D. Manglunki (CERN)

---
Control Room as Open Plan Office
Number of Service Personnel I/II
- Existing GSI Facility Operation:
  - 3 operators for 3 accelerators and ~ 300 m² control room surface area
- Possible FAIR Operation – naïve scaling (minimal automatisation/tuning, truly independent parallel operation, etc.)
  1. MSV 0-3: 7 operators for 8 accelerators and 700 m²
  2. MSV 0-6: 12 operators for 12 accelerators and 1200 m²
- Gretchen Frage: ”How many operators will be effectively needed?“
  - Important boundary conditions:
    - 1 operator doing 24h/7 shift-operation = 7.4 “real/gross” operators (FTEs) = ~ >0.5 MEUR/year → '4+1' vs. '7-8' corresponds to ~2 MEUR/year (+ new offices)
    - 7-8 operators probably mainly needed during peak hours (day) (recommissioning, setting-up of new experiments/beams, etc.)
    - ‘full utilisation during rush hours’ vs. ‘skeleton crew operation’

---
Beam Production Chain & Patterns
Beam Production Chains & Patterns
- Beam-Production-Chain:
  - organisational structure to manage parallel operation and beam transfer through FAIR accelerator facility
  - defines sequence and parameters of beam line from the ion-source up to an experimental cave (e.g. APPA, CBM, SuperFRS, ...)
  - definition of target beam parameters (set values): isotope, energy, charge, peak intensity, slow/fast extraction, …
- Beam Pattern:
  - grouping of beam production-chains that are executed periodically
  - Pattern can be changed within few minutes (target, requires automation for beam-based retuning)
Chains
SIS18
SIS100
HESR
SIS18
SIS100
HESR
Pattern
SIS18
SIS100
HESR

---
FAIR Operation Paradigm I/II
'One Operator per Accelerator Domain' vs. 'One Operator per Experiment':
UNILAC
SIS18
SIS100
CR
Q1
SuperFRS
CR
Q2
pLinac
SIS18
SIS100
p-Target
CR
HESR
UNILAC
SIS18
SIS100
Q3
CBM
UNILAC
SIS18
SIS100
Q4
APPA
UNILAC
SIS18
Qn
ESR etc.
Operator #1
Operator #2
Operator #3
Operator #4
Operator #1
Operator #2
Operator #3
Operator #4

---
FAIR Operation Paradigm II/II
- Option 1: One Operator per Accelerator Domain:
  - Highly-specialised operators (less accellerator physicists needed)
  - High risk of blocking of single operators/‘congestion’ (notably for UNILAC, SIS18 & SIS100)
  - Poor OP utilisation in case only one of 4+ experiments is in operation
  - Less redundancy → permanently more operators are needed
    - 58 vs. 32 Operators (for comparison CERN OP: 90 total)
    - N.B. on OP shift = 7-8 operators ↔ ~ 0.5 MEUR/year
- Option 2: One Operator per BPC/Experiment
  - More efficient machine-machine / machine-experiment interfaces
    - Less overhead, more efficient handover of beam and adjustemtns to exp. Requirements
    - Motivational factor of ‘operator BPC ownership’ (i.e. “my experiment“)
  - Possibility of reduced operation crew (e.g. 32-35 for full FAIR acc. OP)
    - Broader Operator training required (not only machine-specifics)
    - … supported by accelerator experts for setting up of new cycles, experiments and peak-times (e.g. recommissioning after technical stops, etc.)
    - Mandatory semi-automation of frequent accelerator processes (also needed for safe high-intensity operation)
  - Better redundancy withnin OP crew in case of illness, parental leave, holidays, etc.
  - Better value for overall oranisational costs (Skeleton Crew + ‘Acc. Support Team’ when needed)

---
Control Room as Open Plan Office
Number of Service Personnel II/II – Compromise
Proposed FAIR Operation – improved scaling
  - ‘Skeleton Crew’: 4+2+1 people (monitoring, notably during night shift)
    - 4-5 parallel experiments x 1 operator/experiment
    - 1-2 Cryo-Operators (SIS100, SuperFRS)
    - 1 TI Operator (acc. related infrastructure: power network, cooling & ventialtion, Leistungsnetze, media supply, ...)
    - Minimun: assumes setup facility and/or (partial) automatisation
  - ‘Normal Operation’: up to 25 people (machine setup, day-time)
    - 4+2+1 ‘Skeleton Crew’ + accelerator experts:
      - accelerator physicists, RF/BI/CO experts, beam-cooling experts, beam-line physicists, experimentalists, etc.
    - Variable scenarios: + 15-20 People with >4h/day occupancy in FCC
      - setup of new (exotic) beam experiments: typ. 3-4 people
      - failure diagnostics and optimisation of the individual machine, accelerator sub-system, or beam production chain: typ. 3-4 people
      - Parallel machine development: typ. 5-8 people
      - Hardware and Beam (Re-)Commissioning: 10-20 people (?!?)
      - Experiments tightly intertwined with accelerators (ESR, PANDA, etc.): typ. ~ 8 per experiment
      - ...

---
Workstation (designed by CCD)
Workstation Layout
CERN reference concept
CERN experience→ FAIR:
independent fixed displays for each workspace
CCC Ergonomics
Courtesy D. Manglunki (CERN)
3 fixed displays split between 2 workspaces
3 flat screens per workspace
1 mouse
1 keyboard
1 additional admin PC

---
Fixed-Display & Workstation Layout
Information Density Hierarchy
FAIR Facility
Overview
BPC
Overview #1
BPC
Overview #2
BPC
Overview #7
BPC
Overview #8
FAIR Facility
Overview
...
UNILAC
Status
SIS18
Status
SIS100
Status
Super-FRS
Status
CR
Status
HESR
Status
...
60/65“
Fixed-Displays (on wall)
- I: semi-fixed displays – monitoring context, rare interactions (slightly overhead)
  - beam-transmission/beam-loss monitoring, emittance preservation, primary experiment performance index, ...
- II: active user-interaction – automatically adapted to commissioning step (see FC2WG)
- III: non-multiplexed information:
  - Zugangskontrollsystem‘ (ZKS, access system), machine interlocks, ...
Information Density/Level of Detail
2.5 … 3 m
II
semi-static
content
(low user-interaction)
II
I
fully dynamic
content
I
Workstation
multiplexed on BPC
24/28“
~2 m ↔ 120° view angle
III
III
shared workstation
non-multiplexed
III
III

---
Example: FAIR Facility Overview
Proof-of-Concept Prototype
courtesy Achim Bloch-Spaeth

---
FAIR Beam Production Chain Overview
Proof-of-Concept Prototype
courtesy Achim Bloch-Spaeth

---
FCC Workstation Layout
General Concept
permanent usage 24h/7 during OP year
(includes all accelerators, technical infrastructure needed for acc. operation)
Central meeting table:
shift hand-over
small ad-hoc meetings (→ + small meeting room)
social functions
10
reconfigurable usage
storage ring experiments
machine developments
experiments tightly intertwined with acc.
Hardware and Beam (Re-) Commissioning
Fixed Displays
Fixed Displays
12 Workspaces for short-notice stand-by personnel (|| R&D, acc. exp. Students, ..)
(table with data / power connections)
Fixed Displays (on wall)
Primary Accelerator,
Cryo- & TI-Operation
Island/
Bay #1
Island/
Bay #2
4
4
4

---
Fixed-Display & Workstation Layout
tentative distribution of ~25 consoles...
Proposed BPC-Paradigm Sceme:
- 12 – Skeleton-crew (24h/7 OP)
  - 6 parallel BPCs/operators
  - 3 – Cryogenics (non-multiplexed)
  - 3 – Technical Infrastructure (non-m.)
- 5 – Island/Bay #1 – reconfigurable usage
  - storage ring/accelerator-kin experiments
  - machine developments
  - Hardware (HWC) & Beam (Re-)Commissioning (BC)
- 5 – Island/Bay #2 – reconfigurable usage
  - as above
2 – generic short-term consoles (debugging & shift leaders)
Classic scheme (deprecated):
- 5 – primary beam accelerators (UNILAC → SIS18 → SIS100)
- 3 – ESR, CRYRING, CR
- 2 – HESR
- 2 – SuperFRS
- 3 – Cryogenics
- 3 – Technical Infrastructure
- 5 – accelerator-kin experiments
- 2 – generic short-term debugging consoles (+ shift leaders)

---
FCC Workstation Layout
Specific Concept
Need similar user iteration at FAIR:
Accelerator operations, machine experts (& SPLs), GA/TI, experiments, … tbd.

---
Appendix

---
FCC – Executive Summary I/II
primary functional requirements → input to CMP
- mind. 600 m² Nutzfläche
  - Mindestens 5 bis 25 Arbeitsplätze (Vorgaben ASR A1.2 – Abs. 5.4: 12 - 15 m²/Person, 60% effective Nutzfläche → siehe Appendix)
  - klare Kommunikationslinien → offene unbehinderte Sicht (→ frei von Säulen)
- Deckenhöhe: > 3 m (optim. 5 m)
- Doppelboden: mind. 15 cm bzw. 50 cm falls Ent-/Belüftung benötigt
  - N.B. getrennte Lüftung für Raum und Unterboden
- Raumklima: (20-24) ± 1° C, 30-70 % Luftfeuchte, max. 0.1 m/s Luftgeschw.
- Beleuchtung: ≥ 500 lx (regelbar, DIN EN 12464-1, E DIN 5035-7)
  - Gesetzlicher Tageslichtanteil & direkte indirekte Beleuchtung (ggf. Vollspektrumlicht)
- Akustik (Einfluss auf: Bodenbeläge, Wandverkleidungen, Abtrennwände, etc.)
  - Lärmpegel: <35 dB(A) (Hintergrund) bzw. <35-45 dB(A) (10+ Personen, BildscharbV & BAuA)
    - Nachhall-Zeit: 0.4 (best) bzw. max. 0.6 s (DIN EN ISO 9241 – part 6)
    - N.B. Schließt Klimaanlage, PCs, Drucker, usw. ein!
  - Geringerer Rauschhintergrund → geringere Gesprächslautstärken → geringere Störfaktoren für andere HKR Nutzer → bessere Konzentration → ...
- N.B. Elektrische Leistung: ~40 kW

---
FCC – Executive Summary II/II
secondary functional requirements → input to CMP
Kein Einzelobjekt sondern:
- Eigentliche Hauptkontrollraum: ~ 600 m²
- Zusätzliche Flächen
  - Gesetz. 'Pausenraum' bzw. Küche (ArbStättV §6): > 25 m² (optimal: ~ 60 m2)
  - Aufstellflächen für IT/CO Infrastruktur: ~ 200-300 m² ??
  - Kleiner Besprechungsraum (~ 10-15 Personen): ~ 60 m²
    - Unmittelbar an HKR angrenzend
  - Großer Konferenzraum (~ 25 + 25 Personen): ~ 60-100 m²
    - bisher nicht existent bzw. mangelhaft: „Beschleunigerbesprechungszimmer“
    - Kurze Laufdistanz (< 100 m) zum HKR
  - Besuchergalerie für 25 Besucher + Ausstellung (100-200 Besucher/Tag)
  - Abgetrennter Arbeitsplatz für Betriebsleitung: ~ 15 m²
  - Versorgungsflächen & Technische Gebäudeausrüstung: ~ ??? m²
  - Druckerraum (~ 5 m², tbc.)
    - Gesetzlich (BAuA) nicht zwingend für >25 m³ + keine Dauernutzung von Druckern im HKR! (N.B. Meisten Laserdrucker/Kopierer erfüllen Feinstaubpartikel Norm)
- Rezeption?

---
“alt-HKR” & Accelerator Controls Retrofitting
GSI → FAIR Transition in 2018
2018
[Speaker Notes: The initial modularised start version is targeted to be commissioned and ready for physics by 2020. FAIR will extend and supersede the existing GSI accelerator facility which consists of the UNILAC – a general purpose linear accelerator, the SIS-18 synchrotron which will become the booster synchrotron for FAIR, the FRS Fragment Separator, and the Experimental Storage Ring ESR. Many of the FAIR experiments are either fixed-target experiments or experiments that are performed directly inside the storage ring. The SIS100 machine will become the new work-horse of FAIR. It's about 1 km long, a fast-ramping and super-conducting synchrotron that accumulates ions and protons from SIS18 and accelerates them up to a rigidity of about 100 Tesla-Meter. It has a six-fold symmetry, with most of the six long-straight sections being filled up by RF acceleration, bunch compression and bunch rotation systems, or devices related to injection and extraction such as kickers, electro-static and magnetic septa. Most of the SIS18 and SIS100 extraction options are tailored to either: * fast extraction or resonant third-order resonance extraction. We plan to using primarily the knock-out-exciter-based technique that continuously blows-up the beam emittance and pushes particles out of the stable phase-space separatrix.]

---
Beam Production Chains & Patterns
Example II/II
Periodic beam patterns, dominated by one main experiment:
courtesy D. Ondreka
SIS18
SIS100
Unilac
CBM + RIB ext. target (U73+) + AP (LE)
SIS18
SIS100
Unilac
ESR
RIB ext. target (U28+) + ESR
AP + RIB ext. target (U28+) + Biomat
SIS18
SIS100
HESR
Unilac
SIS18
SIS100
Unilac
ESR
RIB ext. target (U28+) + ESR
SIS18
SIS100
Unilac
CBM + RIB ext. target (U73+) + AP (LE)
AP + RIB ext. target (U28+) + Biomat
SIS18
SIS100
HESR
Unilac

---
Accelerator Experience & Efficiency
1995-2016: U. Scheeler, S. Reimann, P. Schütt et al.
constant
~ 75 ± 5 %
long-running “static”
experiments
Many || experiments
re-configuration ~ 1-2 weeks
→ FAIR base-line
*
Based on: U. Scheeler, S. Reimann, P. Schütt et al., “Accelerator Operation Report”, GSI Annual Scientific Reports 1992 – 2015 + 2016 (D. Severin)
https://www.gsi.de/en/work/research/library_documentation/gsi_scientific_reports.htm
N.B. ion source exchanges are factored out from UNILAC & SIS18 data (~ constant overhead)
Availability: experiments + detector tests + machine development + beam to down-stream accelerators;
Down-time: unscheduled down-time + standby; Operation: accelerator setup + re-tuning
* 2018 operation limitations:
only ½ UNILAC (w/o A3 & A4)
only 1 element in SIS18
Therapy Operation
(different accounting)

---
FAIR Challenges & Constraints
… SIS18 Operation Experience & Efficiency
Beam-on-Target figure of merit (FoM) of ~75% → FAIR-BoT (efficiency εFAIR):
%varepsilon_{"FAIR"} ~:=~ prod from{i} to{n_{machines}} %varepsilon_{i} ~=~~ %varepsilon_{"UNILAC"} cdot %varepsilon_{"SIS18"} cdot %varepsilon_{"SIS100"} cdot %varepsilon_{"SuperFRS"} cdot %varepsilon_{"CR"} cdot %varepsilon_{"HESR"} cdot ...
+ new operational challenges:
operating beyond present beam parameter envelope, x10-100 higher intensities, x10 higher energies → machine protection & losses/activation become an issue
“… have to improve!”

---
FAIR Control Centre
Tentative Project Planning (2.14.17.2)
media event
2025

---
FAIR Commissioning & Control Project
project lead: R. Steinhagen (deputy: S. Reimann), since PBL-JF 21.03.2015, project ID: 2.14.17
Scope: coordination, development and follow-up of a coherent and sustainable concept, strategy and technical guide-lines/specifications for
1. Commissioning1,
2. Control2, and
3. Operation
 of the whole3 FAIR Accelerator Complex
- Broken down into 2 Work Packages:
  - 2.14.17.1 FC2WG -- FAIR Commissioning & Control WG (link to: 2.14.10.1, 2.14.12.x 2.x.[3,4,6,7 & 12])
    - development, engineering check of the concepts and functional guidelines (acc. tech-experts, equip-GL)
    - EDMS signatory process:: MPL, MKs, main equip.-GL, head FC2WG (as approval leader)
  - 2.14.17.2 FCC-WG – FAIR Control Centre WG (link to: 2.14.10.10)
    - technical control room infrastructure: consoles, furniture, IT infrastructure, etc. (mainly CO-IN, OP, Exp-reps.)
    - Machine-Civil-Construction Interface (↔ 'Campus Master Plan')
1 commissioning covering the initial commissioning, subsequent re-commissioning & assisted operation phases (prior to 'regular operation')
2 N.B. 'control' here dt. “Anlagenkontrolle”
3 including all existing GSI and future FAIR accelerators as well as machine-experiment specific CO interfaces (e.g. target steering, spill control, data exchange)
pre-2016 Project structure
2.14.17.1
PBL-JF

---
FAIR Commissioning & Control WG
http://fair-wiki.gsi.de/FC2WG/
focus in 2016
Commissioning
focus in 2015
FAIR Commissioning & Control Working Group
platform to discuss, coordinate and work-out FAIR commissioning and operation
open to all who can participate and contribute to this subject!

---
FAIR Control Centre Working Group
Functional Organisation – Proposal for Discussion
GSI/FAIR Directors
Weyrich,
Langanke, Blaurock
FCC-WG Nutzergruppen – „Rollen“:
- PL Bau/Civil Engineering
  - bis Leistungs-Phase 2: K. Berkl
  - ab Leistungs-Phase 2: N.N.
- FPL TGA: Elektro N.N., HLS N.N., BMA N.N.
- HPL: R. Steinhagen (Vertretung: S. Reimann)
- Vertreter Fachabteilungen:
  - Operateure Beschleuniger: 2 x N.N.
  - CSCO-IN: R. Vincelli (R. Bär)
  - SIS 18/100: N.N. (Bereich Spiller, tbc.)
  - Kryo: H. Kollmus (C. Schroeder)
  - Exp.: I. Lehmann, D. Severin
  - TI/GA: N.N. (Bereich Trumm, R. Becker)
  - Öffentlichkeitsarbeit: I. Peter
?
pre-2016 Project structure
Campus Development
G. Stephan
PBL-JF
func. requirements → input to Campus Masterplan
R.Steinhagen
K. Berkl
FCC-WG
2.14.17.1
2.14.17.2
CSCO
Infrastructure
R. Vincelli
10 members, tbc.

---
- Similar Complexity to CERN
- @FAIR:
  - Additional complications/constraints
    - much higher intensities → machine protection/activation becomes an issue
    - facility complexity
    - limited personnel
  - Q: are we ready?
  - Q: How to optimise commissioning, control & operation → FC2WG
  - Q: can we ramp up the expertise/operation to be ready for FAIR (SIS100 within 5 years)
  - Q: strategy to shape a commissioning facility-wide team → FCC is one key aspect in this
optional → remove?!?

---
FAIR-HKR: Rahmenbedingungen
… muss den Routine-Betrieb aber auch Stoßzeiten* und langfristig weitere (realistische) FAIR Ausbaustufen unterstützen:
1. Deutlich mehr Platz benötigt:
  1. verschiedene Analysen → bis zu 25 Arbeitsplätze (600 m²) benötigt
  2. Nachhaltige Planung → Campus Master Plan
Öffentliche Darstellung der GSI & FAIR
Einfluss: Effizienz Beschleunigerbetrieb↔ FAIR Performance
Vision Statement: Ein HKR für Alle
* (Erst-/Wieder-)Inbetriebnahme, Aufsetzen von neuen Experimenten/Strahlen, Maschinen Entwicklungs Perioden…

---
FAIR-HKR: Warum? I/II
Deutlich mehr Platz benötigt; Nachhaltige Planung → Campus Master Plan
  - GSI-HKR heute: 3 Beschleuniger → FAIR: 8/11+ Beschleuniger
    - + höhere Komplexität & neue Cryo- und andere technische Infrastruktur
  - Inbetriebnahme von neuen Beschleunigern muss parallel zur regulären Strahlbetrieb möglich sein
  - Zugehörige Infrastruktur: Besprechungsraum & Konferenzraum
Öffentliche Darstellung der GSI & FAIR:
  - Psychologie: Qualität der Forschung ↔ Qualität der Repräsentation der Anlage
  - Aber auch: Vielschichtiger Motivationsfaktor der Angestellten/Besucher
  - Öffentlichkeitsarbeit – Plan für FAIR Erfolg: 30.000 Besucher/Jahr (150/Tag, N.B. CERN > 70.000)
    - Bestehender GSI-HKR ist inkompatibel mit Besuchern

---
FAIR-HKR: Warum? II/II
Einfluss: Effizienz Betrieb↔ FAIR Performance
  - Minimierung von Störelementen, Ablenkungen, und Fehlbeanspruchungen der Mitarbeiter
  - Effiziente Kommunikation: Management, B. & E. Physiker/Ingenieure, und Betriebspersonal
Vision Statement: Ein HKR für Alle	→ deutlich verbesserter/reduzierter Kommunikations-Overhead (CERN Erfahrung)
  - Bessere Koordinierung von Strahl-Übergabe Schnittstellen
  - Effizientere Anpassung der Beschleunigerkette an sich ändernde Anforderungen
  - Know-How Transfer von Beschleuniger/Experiment-Experten zum Betriebspersonal
  - Regelung des 'Hoheitsproblems' (Beschleuniger-Verantwortlichkeit)