Digitization of Analog Signals @ FAIR
– Initial Concept, Strategy and Next Steps –

---
Poka-Yoke (ポカヨケ) – 'Mistake-Proofing'
Reaction-Time and Cost → “fix” errors early
Fix problems early, when and where they occur
- Minimises procrastination of errors: “Safety starts with safe habits”!
  - big losses with big intensities	→ bad (activation)
  - large losses with small intensities → probably OK? … No!
    - requires paradigm change!
  - Interdependence between beam parameter & systems
- Early indication of developing/not-yet-critical faults:
  - Post-Mortem analysis ('as good as new' SIL assurance)
  - Preventative maintenance
  - fix “domino effect” problems at the source not its symptoms
    - e.g. fix problems with low-intensity beam rather than with high-intensity beam (avoids revalidation of loss patterns, MPS setup, …)
    - e.g. fix basic accelerator parameters before moving on to higher-order effect (e.g. extraction/injection energy/trajectory → orbit → tune → chromaticity → optic → … → driving terms
time until the problem
was discovered/fixed
costs

---
FAIR Protection Hierarchy
Sequencer
& operational
procedures
SW-Interlock System
(MASP)
HW-Interlock System
(FBAS)
FAIR
Machine & System
Design
BPF
BPF
SBF
SBF
SBF
prevent scheduling of
cycles that would
interlock
prevent injection of
similar beam during
next cycle
Poka-Yoke
Error proofing
Availability opt.
Convert 'ultra-fast' to
fast errors
10s of seconds → minutes/hours
~ 100 ms
50 us
< turn
time-scales:
Beam Current Transformer – I(t) & dI(t)/dt
BLMs
BPMs (tbd)
Beam Transmission Monitoring
Vacuum
Cryo
QPS
Beam Quality Monitor (εx/y,εs, …, tbd.)
Main Dipole/Quadrupole
Main Sextupoles
Corrector Magnets/Steerer
Beam Presence Flag
Machine-Mode dependent
Interlocks (i.e. transfer-line)
Material Choice
Accelerator & Beam Modes
Management of Critical Settings
Slow Beam Quality Checks
Collimation/Halo Cleaning
Beam Parameters
Accelerator Optic
… other equipment self-monitoring
Intensity Ramp-Up
Post-Mortem Analysis
aka. “as good as new” verification

---
Digitisation of Analog Signals
- Primary goal: static operation i.e. w/o need to reconfigure device for given measurement purpose
  - generic facility wide & WR-timing-synchronised software-oscilloscope
  - systematic performance monitoring & statistics,
  - Interlocking & first-line error diagnostics
    - 100% semi‑automated dry‑run test coverage, …
  - Beam‑based feedbacks
    - 2018-goals/proof-of-concepts: Multi-Turn-Injection (MTI) & extraction optimisation
  - also: pre-requisite prior to major ‘alt-HKR’ upgrades and/or move of operations to FCC
- Sub-categories:
  - a) time-domain: functional actual-vs-reference monitoring (DC – up to 200 MHz)
  - b) frequency-domain: SA- & VNA-type funct. Δfbw≈20 MHz@fLO≈DC…6 GHz
  - c) video-signal (IPM, screens, etc.) → not covered
    - existing BI technology/integration, main issue: budget/MC commitment
    - need interim solution for ‘alt-HKR’ retrofitting → personell resources needed
  - d) generic signals < 1 MHz bandwidth → also not covered
    - different strategy: local low-cost high-ADC-density controller, ...
- Not a new concept: existing “Soft Oscilloscope System” specification https://edms.cern.ch/document/1176042/3
  - some smaller updates and detailed interface descriptions needed

---
Main Paradigms
traditional/old concept (underlying assumption: scopes/digitizers are expensive, RF switches are cheap)
targeted concept (underlying assumption: scopes/digitizers are cheap, RF switches are expensive)
~10 €/m
(short)
250-500 €/ch.
2-3 k€/ch.
200 -1000 €/ch.
was > 100 €/ch.
~ 200 €/ch.
~10 €/m
(long)
device #1
Front-End
(FESA, C++)
device #1
digitizer
device #2
device #2
digitizer
~ 0.5 k€/ch.
...
...
Front-End
(FESA, C++)
device #(n)
device #(n)
ethernet
~ 10 MB/s
digitizer
Front-End
(FESA, C++)
e.g. USB
~ 60 MB/s
2-3 k€/ch.
device #(n+1)
Front-End
(FESA, C++)
device #(n+1)
digitizer
...
...
Controls/
Operation
device #(n+m)
Front-End
(FESA, C++)
device #(n+m)
digitizer
on-demand measurement
(selected signals, error-case, …)
con:
high-reconfiguration overhead (manual)
limited test-coverage, trending
permanent monitoring
(error-case, trending, interlocks, beam-based feedbacks, …)
Controls/
Operation
RF Switch
BLL: Brain-Locked-Loop
Not routinely connected
(only error case)
flexible
grouping option
feedbacks

---
Documentation of Operational Usage
UNILAC & SIS18
Kaufmann, Reeg, Roedl, Steinhagen, Wiessmann et al.
SIS18 upgrade
list & priorities
for 2018
Kaufmann, Steinhagen et al.

---
Example: CERN OASIS – Concept
https://wikis/display/OASIS/Home

---
Example: CERN OASIS – Concept
In essence a
directory service:
“I need signal X” →
“found at <FE-’Y’:slot ‘N’>

---
Digitisation of Analog Signals
Next steps I/II – SW/Controls Integration
- initially: use of out-of-the-box OEM software → min. SW integration effort
- FESA-fication ready for 2018-restart (CO strategic target, R. Bär)
  - functional specifiation, review, preparation for tendering by June’17
- minimum SOS functionality
  - a) segment acquisition after injection (aim: static configuration per BPC & channel)
    - sequence: prepare event/arm → fixed WR timing trigger event → capture ‘n’ kSamples → publish via CMW/FESA → repeat (if applicable)
    - setting of AFE gains, time scale, ...
  - b) extraction timing event (re-aligning w.r.t. actual extraction event)
    - as above, but in addition re-align extraction data to actual extraction event
  - c) continuous acquisition during cycle (injection → extraction, primarily RF cavities)
    - prepare event/arm → fixed WR timing trigger event → stream data to FESA → data reduction/post-processing → publish (FESA interface similar to BCTs, BPMs, ...)
- extended functionality, simple post-processing of data, e.g.
  - ‘actual vs. reference’ comparison
  - simple demodulation (→ RF amplitude, phase and frequency monitoring/interlock)
  - simple FFT power spectrum @ e.g. 1k, 100 & 10 Hz (overlap to be discussed)

---
Digitisation of Analog Signals
Next steps II/II
- Time-Domain:
  - review functional requirements/technology options → next FC2WG meeting
    - aim at dedicated digitizer for every operationally relevant channel (→ fixed config)
      - limit: not every sub- but relevant functional surveillance of devices, e.g.
        - RF cavity gap voltage → RF amplitude, phase-difference, frequency
        - RF Extr./Inj. kicker	→ pulse-shape and timing of every kicker module
    - Digitizer options: primarily looking for options for SIS18 in 2018, but strive to keep choice compatible with ESR, Cryring, UNILAC (!?!) & other future accelerators
      - minimise CO/BI/SYS ... integration effort, maintenance, ...
  - technology decision → end-2017-Q1
    - follow-up of procurrement for 2018
  - Specification of specific functional user-requirements ongoing → let yourself be known if you want to get involved
- Frequency-Domain:
  - Software-Defined-Radio (SDRs) seem to be nice alternative to SA & VNA
    - good performance, software support, out-of-the-box functionality, extentability (→ ‘GNU Radio’, popular in HAM/RF community)
    - need a bit more evaluation & notably AFE specs from ESR, CR, … to check compatibility with available systems.
  - minimum frequency-domain diagnostics ()
    - a) SA → reference: existing CERN BBQ FFT FESA integration (+ exciter control)
    - b) VNA → reference: existing CERN BBQ PLL FESA integration (+ exciter control)
  - Specification does exist but more in a draft stage: please, please let yourself be known if you want to get involved and help with the evaluation
- Video Signals: ???
  - Focus on 2018: ‘Intermediate solution’ vs. ‘nominal integration’ (€)

---
Anatomy of FAIR Acc. Control System
R. Baer (department head) et al.
FAIR Facility Overview
('Page 1')
Applications
(Java)
Exp. Apps.
(Java)
Applications
(Java)
Applications
(Java)
Applications
(Java)
Applications
(Java)
Applications
(Java)
Applications
(Java)
common generic API
short-term
(few weeks)
LSA-DB
Layout
DB
(???
SCADA
(for prop. HW,
e.g Cryo.)
LSA
(Settings Mgmt)
(Java)
Archiving
(Java, C++, tbc.)
long-Term
(years → ∞)
JAPC (CMW = ZeroMQ-based)
Timing
(FESA, HW, C++)
Prop. HW
(non-FESA)
Front-End
(FESA, C++)
Front-End
(FESA, C++)
...
White Rabbit
actual HW
actual HW
actual HW
Machine-Protection, Interlocks, MASP
Transmission Monitoring, Post-Mortem
Tier 3: Industrial Control & IT
(aka. Front-Ends)
Tier 2: Business Layer
(Control Logic)
Tier 1: Application/Presentation