2017-09-20 FC2WG Meeting #31
Common Specification F-CS-C-0002e:
Digitization of (generic) Analog Signals
in the FAIR Accelerator Complex
– Status & Next Steps –
https://edms.cern.ch/document/1823376
R. J. Steinhagen
with input from: R. Bär, C. Handel, J. Fitzek, D. Ondreka

---
Scope
- FAIR and notably the FAIR Control Centre will deploy a ‘fully-digitial’ control paradigm:
  - automatic monitoring
    - performance tracking & early fault detection
    - quantitative/semi-automatic feedback and setup applications
  - assisted isolation of HW faults (‘ref-actual’-monitoring)
  - remote expert diagnostics (as needed)
- Primary goals
  - generic abstraction of the vendor-specific digitizer software interfaces (explicitly open for new/future vendor/digitizer models extensions)
  - limited range of generic data post-processing on the acquired data
  - control system integration by providing standardised FESA interface
- Secondary goals
  - simplify further extensions, compactness, readability, re-usability, testability, and maintainability of the FESA implementation
  - Use of open-source signal processing and data fitting libraries
    - GNU-Radio – frame-work:	https://www.gnuradio.org
    - ROOT – frame-work:	https://root.cern.ch

---
Some notes on: Specifications, Engineering Check & Approval Procedures I/II
- Common Specification – CS
  - collection of functional user requirements
    - usually facility wide accelerator domain (letter ‘B’), for Digitizer spec domain CO (letter ‘C’)
  - system integration into the facility control and operation concepts
    - primarily reduced to interface description (where necessary)
  - deliberately HW agnostics → view on long-term FAIR base-line
    - keep it open for upgrades, new HW devices or different implementation options
- Detailed Specification – DS
  - specific HW/SW requirements
  - extension of interfaces & requirements not covered by CS
  - handling of additional legal contractual obligations (if not already part of another higher-level specification)
  - FAT/SAT procedures (for ‘in-kind’/external contracts)
- Conceptual Design
  - concrete implementation/interface (usually done by ‘in-kind’ or external partner)
  - extension of interfaces & requirements not covered by DS
  - pre-requisite for the Final Design Review & ‘go-ahead’ for the implementation

---
Some notes on: Specifications, Engineering Check & Approval Procedures II/II
Process:
collection of signature
Management
(middle tier)
Approval
Approval Signatories:
SPL – primarily acc.(-related)
Machine Coordinators
acc. Group Leader	affected primarily by this (financial & personnel, ...)
notably: Controls, OP, BI, …
N.B. this includes presently >18 required signatures!!!
collection of signature
FC2WG
Engineering
Check
review/iterate
technical solutions
task groups
typ. 4-5 experts
wider accelerator expert community
via: FC2WG meeting & FAIR-C2WG-ALL‎@gsi.de
(N.B. includes SPLs, MCs, acc. GL, management, ...)
formal engineering check/approval
tracked by EDMS
informal engineering check/approval
tracked by EDMS
focus on technical aspects
planning/resources/legal aspects

---
Main Paradigms
traditional/old concept (underlying assumption: scopes/digitizers are expensive, RF switches are cheap)
targeted concept (underlying assumption: scopes/digitizers are cheap, RF switches are expensive)
~10 €/m
(short)
250-500 €/ch.
2-3 k€/ch.
200 -1000 €/ch.
was > 100 €/ch.
~ 200 €/ch.
~10 €/m
(long)
device #1
Front-End
(FESA, C++)
device #1
digitizer
device #2
device #2
digitizer
~ 0.5 k€/ch.
...
...
Front-End
(FESA, C++)
device #(n)
device #(n)
ethernet
~ 10 MB/s
digitizer
Front-End
(FESA, C++)
e.g. USB
~ 60 MB/s
2-3 k€/ch.
device #(n+1)
Front-End
(FESA, C++)
device #(n+1)
digitizer
...
...
Controls/
Operation
device #(n+m)
Front-End
(FESA, C++)
device #(n+m)
digitizer
on-demand measurement
(selected signals, error-case, …)
con:
high-reconfiguration overhead (manual)
limited test-coverage, trending
permanent monitoring
(error-case, trending, interlocks, beam-based feedbacks, …)
Controls/
Operation
RF Switch
BLL: Brain-Locked-Loop
Not routinely connected
(only error case)
flexible
grouping option
feedbacks

---
Digitization of Analog Signals at FAIR and SIS18 in ‘18
Detailed Integration Specification → in-kind contract
released for formal
approval tomorrow

---
General Signal-Flow Scheme
N.B. GNU-Radio real-time streaming processing inspired
Data Source
(post-) processing B.x)
Data Sink
module ID #1 + parameter set #1
channelName-ext #1
channelName
e.g. ...
module ID #2 + parameter set #2
channelName-ext #2
- Scheme can be further cascaded and combined with other modules
  - based on GNURadio‘s signal-flow concept https://www.gnuradio.org/
    - N.B. there are conceptually also other similar other projects: e.g. ADS, QUCS, Spice, LabVIEW … but with a different non-real-time (RF) signal processing
(post-) processing B.y)
Data Sink

---
From the Specification (V 1.0)
https://edms.cern.ch/document/1823376/
- Two data acquisition modes:
  - A.1) Streaming-mode acquisition
  - A.2) (Rapid) block-mode acquisition
- Limited set of post-processing modules:
  - B.1) raw-measurement scaling and offset shift
  - B.2) time-base re-alignment (lag & extr. event offset compensation)
  - B.3) data aggregation and decimation (typ. to kHz → Hz)
  - B.4) real-time Short-time Fourier Transform (STFT)
  - B.5) amplitude, phase and frequency detection (I-Q demodulation)
  - B.6) χ2-type fitting and basic peak detection
  - B.7) actual versus reference comparison → interlock

---
Data Acquisition, Client Interfaces & Synchronisation
similar to/the same as
BPM, Trafo, BTM, handling
indiv. HEBT-in trajectories
published per injection
time (not to scale)
Circular Machine Cycle
e.g. SIS100, CR, HESR, CRYRING, SIS18, ESR
transfer line 1
e.g. SIS18 → HEBT → SIS100
or: SIS18 → HEBT → ESR
or: ESR → HEBT → CRYRING
transfer line 2
e.g. SIS100 → HEBT → p-target/CR
or. SIS100 → HEBT → CBM
beam/batch intensity [ppb]
HEBT rigidity
beam rigidity
FAIR Timing:
timing: prepare
timing: start ramp
or tn+1
timing: injection t1
timing: end ramp
 or tn+2
timing: extraction
('beam-out')
 or tn+3
timing:
Merging/rotation #2
timing:
merging/rotation #1
timing: injection t2
timing: injection t4
timing: start segment
('beam-in', t:=0)
orbit acquisition @ 1 kHz (100 Hz, 10 Hz, 1 Hz, N.B. batch average)
1st
2nd
3rd
4th batch
extracted beam (slow)
N.B. being discussed/proposed:
bunched beam (≥100 MHz)
during slow extraction
indiv. HEBT-out trajectories
published per extraction
extracted beam (fast)
trajectory acquisition

---
Low-Level Acquisition Modes
A.1) Streaming-mode acquisition I/II
acquisition schematic:
aggregated data
BPs
BP / #1	BP / #1			...			BP / #1	BP / #2	BP / #2			...			BP / #2	BP / #3					...					BP / #3
low-level BPM digitizer data
N.B. ~250 MS/s
FESA server tasks/secondary RT tasks
real-time task/BPM FPGA
time
timing event
BP #1 start
timing event
BP #2 start
timing event
BP #3 start
timing system/
receiver
user-interface (JAPC)
FESA server tasks
post-
processing
post-
processing
e.g. instant orbit,
closed orbit@ < 1 kHz,
...
post-processed data
timing event
user-defined
user-defined
fast (70 MS/s)
acquisition

---
Generic Acquisitions I/II
Specified FESA Data Streams
Following modes of acquisition would be expected to be served simultaneously (though some of them could be implemented as down-sampled copies of the higher bandwidth acquisition):
1. Slow-acquisition (FESA property: ‘Acquisition’) – sub-choices (selected via CMW-filter):
  1. 'Sequence' acquisition between ‘beam injection’ and ‘beam extraction’: the specific signal averaged and decimated to the rate needed for the given client (e.g. 1 kHz). → property notifies complete trace as a function of time at the end of the sequence (up to 30-60 s)
  2. ‘Continuous’ real-time data publication during the cycle (↔N.B long SIS100 cycles and/or storage rings): → property notifies single measurement at typical update rate around 10-25 Hz
    1. use-case: user-level applications (inj./extr. steering), software-based real-time feedbacks, ...
  3. ‘Instant’ signal acquisition: → property notifies single measurement at pre-defined time delays (ms-scale)
    1. software interlock on injection/extraction orbit deviations (via MASP)
2. Fast block-mode acquisition (also ‘Acquisition’):
    - up to 10 external user-defined timing triggers per sequence (ie. each injection, extraction etc.)
      - corresponding CMW property subscription: e.g. ‘TRIGGERED’ or name of specific timing event
    - horizontal channel settings are assumed to be fixed per digitizer
Post-Mortem (FESA property 'PostMortem'): not finalized but provisionally:
  1. first circular buffer storing each signals @ 1 kHz for the last second of beam or full cycle
  2. second circular buffer storing the last 1k (10k?) turns at maximum sampling rate

---
Signal Flow-Graph → SAT I/II

---
Signal Flow-Graph → SAT II/II

---
Time- & Frequency-Domain
Acquisition Interface
↔ same style as other acquisition
systems: BPM, Trafos, ...
- Interface defined per ‘signal’ ie. signal name is part of subscription filter property
  - short term: full list of available signals via ‘ChannelDescription’ Property & Java API (2018)
  - long-term: ‘name server’ type service (upgradability/extension)

---
Documentation of Operational Usage
UNILAC & SIS18
Kaufmann, Reeg, Roedl, Steinhagen, Wiessmann et al.
SIS18 upgrade
list & priorities
for 2018
Kaufmann, Steinhagen et al.

---
2018 Digitizer Deployment & System Distribution
as agreed with MC & Controls
- + all “AEG” power-supplies in BG2.002 (in conjunction with EPC/CO)
  - N.B. >2018: SIS18 MC (P. Spiller) requested budget to complete digitize all SIS18 non-ACU/legacy power-supplies (to be implemented after beam-operation) → in 2019: SIS18 should be fully digital & ready for moving operation to the new FCC
- + some prototype studies for Schottky diagnostics @ESR (Sanjari et al.) and @CryRing (W. Kaufmann et al.) … if time permits

---
Main Digitizer Selection Criteria I/II
… analysed digitizers from >54 companies for:
- Controls Integration (what concerns initially by CO-supported devices):
  - support/availability of Linux drivers, compliance with Linux driver standards, and tracking of mandatory kernel (and security) updates
  - no non-embeddable solutions ↔ significant resource overhead related to integration & maintenance. Primary issues related to Windows/oscilloscope-based options (also CERN experiences): 24h/7 reliability & IT security costs for the remote-controlled operation
    - N.B. some devices may not be reached at the installation site during the beam operation, > 100 systems total
  - minimization of the targeted system platform heterogeneities (minimisation of system/driver dissimilarities)
- Electrical and RF aspects (↔ based on existing system and accelerator operation analysis)
  - analogue bandwidths between 20 MHz, 200 MHz, up to at least 500 MHz
  - full RF AFE with selective gain and offset adjustment
  - >7 ENOB for high bandwidths and/or near thermal noise for lower bandwidths (→ 8-bit up to 16-bit digitizers)
    - better resolution and early detection of system errors and/or accelerator parameter drifts before these may potentially lead to faults with longer down-times
  - fast multiple triggering of measurements with dead times below 2 us
  - min. 1 preferred >8 external digital trigger/signal inputs (fast status detection of fast timing/RF feedback parameters)
- Numerical performance requirements:
  - real-time data streaming, bandwidths > 60 MS/s ↔ multi-user capabilities & enables easy SW-based post-processing (N.B. also availability of SW-savvy personnel vs. scarce VHDL expert resources at GSI/FAIR)
    - NB this being another exclusion criterion for Ethernet-based oscilloscopes
  - preferred USB 3.0 interface connection (bandwidth, scalability, long-lasting standard, interface costs, space constraints)
  - optional: possible modification of the digitizer FPGA firmware (↔ permits future extensions/pushing SW post-processing to HW)
- Mechanical form factor
  - stand-alone digitizer with a maximum of 19" width and 1U-height ↔ actual available space in the the planned rack/system locations

---
Main Digitizer Selection Criteria II/II
- Qualitative vendor criteria
  - products must (largely) be already available ↔ no R&D (re-commissioning risk minimisation)
  - proven long-term experience in T&M instrumentation
  - sustainable, adapted & consistently further developed product range ↔ minimisation of future heterogeneity
  - broad market coverage ↔ sustainable supply source for for re-orders & extensions
  - prefer manufacturers from the EU and/or FAIR members
  - no vendors targeting price dumping
- Digitizer Costs target (excl. FEC/timing related costs):
  - < 700 EUR/channel respectively 3000 EUR/system (consisting of 4 channels @ 200 MHz)
  - scalability for FAIR, not yet foreseen systems, upgrades, external non-acc users, ...

---
Final Vendor/Model Selection
PicoScopes from Pico Technology
- Low-Bandwidths (< 20 MHz)
  - PicoScope 4824, 7 (8) channels, 11.3 ENOB @ 20 MHz)
    - N.B. ~ 16 ENOB @ 10 kHz (ΔI/Imax ~ 10-5)
  - 2018: primarily used for EPC-related systems (→ 2018: “AEG”)
    - planned to digitize: Iref, Uref, Iactual, Uactual, ΔI, Uint, + 1 spare
    - 8th channel for WR timing synchronisation
- Medium-range Bandwidths (< 200 MHz)
  - PicoScope 3403D MSO ↔ 3406D MSO), 4 ch, 6.9 ENOB @ 200 MHz
    - N.B. ~ 7.9 (15) ENOB @ 10 MHz (10 kHz) (ΔU/Umax ~ 10-3 (3·10-5))
  - 15 (16) digital channels → triggering e.g. on fast RF loops states, etc.
  - 2018: primarily for Ring-RF (→ “Gap Voltage”) and HV-extraction kicker trigger acquisition
- High-Bandwidth (< 500 MHz, (1 GHz))
  - PicoScope 6402C↔ 6404C, 4 channel, 7.3 (7.9) ENOB @ 500 (200) MHz
  - 2018: primarily used for HV extraction and tune kicker waveform
- Open: specification for further digitizer devices
  - tentatively: Ettus Research SDR for spectra-related applications
N.B. Ordered/deploy 39 digitizer for 2018, pending 40 more for >2018 (SIS18 EPC upgrade)

---
19” Mechanical Digitizer Integration
For 2018 this will be done in-house	(too small quantity for supplier, but open for future orders/models)
Key-aspects (to be finalized):
- 19”-1U form-factor
- mechanical connector adaptation
- digital IO adapter board (e.g. trigger 2x10 pin→ Lemo (terminated))
- double-redundant PSU	(e.g. Traco, >1 Mh MTBF each)
  - single-/split-connection to power network ↔ meet same FEC standard
- Health-Monitor-Interface (HMI)
  - for remote reset
  - simple non-OP control tasks
- Front-Panel labelling/etching etc.

---
Tentative Front-End Server Platform
choice of Accelerator Controls Group
HP Proliant DL 180 (380) Gen9++
- 2U height, disk-less (tbc.)
- high-performance options:
  - Xeon 2620V4, 2.1 GHz, 8 cores
  - single-/dual-CPU option
- Main reasons for choice:
  - high redundancy: ~ 1 Mh MTBF
  - low integration, administration & maintenance overhead (N.B. ILO integration for >150 server, limited personnel for routine maintenance tasks → optimisation of personnel resources)
< 80 cm
to be confirmed

---
Conclusions
- Main focus: generic acquisition and common post-processing of analog signals in the range of a few MHz to hundreds of MHz (in theory: also > GHz)
  - vendor-specific HW abstraction (→ future upgrades of newer version or different models)
  - two basic low-level acquisition modes: continuous & rapid block-mode
  - set of 6 post-processing modules
  - maintainability & testability (unit testing, testing, testing, ...)
- Next steps:
  - (informal) ‘Engineering Check’ via FC2WG (& in-kind partner)
  - formal ‘Engineering Check’ via EDMS (↔ collection of signatures of those who gave feedback)
  - formal ‘EDMS Approval’ (↔ collection of signatures, tomorrow)
  - Integration contract being already prepared, SAT targeted Q4’17/Q1’18
  - Specific deployment/preparation → Dec’17/Jan’18
  - First early tests during Dry-Run in February/March 2018 (EPC “AEG” re-commissioning)
- Open Items (N.B. not just digitizer, but also other systems):
  - handling of 3D-data structures in FESA: Japc, Archiving, …
  - transmission of extraction event meta-information (via timing message, data-supply, … ?)
    - staged not for 2018
  - ‘Form’ over ‘Performance’, but should define a minimum standard and practical upper-boundary (engineering margin)
    - parallelisms, FEC platform, ...
  - ...

---
Appendix