2015-04-13 – V1
2015-11-13 – V2
SIS100 BPM
Analysis of Use-Cases & Requirements
Ralph J. Steinhagen, David Ondreka

---
SIS100/18 BPM Topics to be discussed
P. Kowina, D. Ondreka, R. Steinhagen
- Pick-ups: TFS & Head-Tail BPM + warm quadrupoles
- AFE improvement ↔ SIS100 nom. beam operation/parameter
  1. RF Hybrid → robust electrical BPM centre (common mode rejection > 40 dB) & higher sensitivity (>10)
    - digitize 'amplified Δ' vs. 'A ~ Σ (v. large) ± Δ (~1% w.r.t Σ)'
  1. RF Low-Pass → reduce req. dynamic range
    - compatibility with nominal bunch-length variations
  - Rationale: operationally robust orbit steering, inj./extr. steering, optics-via-Δμ-advance + intensity variation margin
- DAQ – LOBI & SP/OP use-case analysis
  - need to measure/control beam during whole cycle (injection → extraction)
  - frev turn trigger/tagging, inj./extr. synchronisation
  - FESA interface for: orbit, injection/extraction steering, 10k-turn analysis, MDs
    - similar to FCTs & BPM → could become prototype for other ring BI
    - 1 kHz closed orbit (per-cycle, @10/25 Hz), first 1k (10k?) turns, last 100 turns, 10k study buffer (arbitrary timing event during cycle)
  - compatibility of orbit & trajectory with Q/Q' acquisition
- CO Controls Integration
  - data concentration, buffers, HW/SW interlocks
  - Archiving & PM (which data? Turn-by-Turn data?)
  - Machine Protection information gathered by BPM system: threshold criteria? time for reaction to FBAS? HW/SW Interface?
  - FESA acquisition paradigm (change from 'virtual accelerator' → 'beam production chains')
- Automated Steering
  - Slow cycle-to-cycle orbit & trajectory control (base-line: work ongoing)
  - Fast in-cycle real-time orbit feedback (is it needed?)

---
Observables: Orbit (avg. Trajectory)
- Global orbit – minimise the aperture requirements; monitor/log closed orbit
- Local orbit at critical points – fine control of aperture limits (collimators, septa, etc.)
- Machine Alignment – beam-based alignment of quadrupoles, BPMs etc.
- Linear optics model↔ LOCO (N.B. rel. slow method)
  - Integer tunes – Fourier analyse of closed orbit
  - Dispersion D(s) – closed orbit versus momentum deviation
  - measure β(s) and μ(s), BPM & orbit corrector calibration, polarity checks
  - search for optics imperfections
- Non-linear optics model: b2/a2 to b5, b3/a3 etc.
  - polarity checks of higher-order multipoles
  - optics linearisation

---
Observables: Trajectory and Oscillations
- Trajectory – beam threading, close trajectory on itself, visual inspection
- Position and momentum error at injection
  - Subtract orbit from first-turn trajectory and compute x,px,y,py at injection (injection matching)
    - N.B. this includes also HEBT BPMs
  - Deduce momentum from trajectory averaged over the azimuth → controls the SIS18/SIS100 energy matching
- Linear optics model↔beta-beating via. phase-advance measurement (N.B. rel. fast method)
  - measure β(s) and μ(s) at injection, ramp, extraction, optics changes due to γt shift
  - search for optics imperfections
- Phase space measurement
  - separatrix of slow-extraction → sextupole adjustment: amplitude & phase
  - dynamic aperture, driving terms
- Local chromaticity
  - Dependence of β(s) and μ(s) on momentum for the measurement of b3 versus azimuth
- Local impedance – dependence of μ(s) on beam intensity
- Local coupling – Identify the local 4D transport matrices
- Optional/complementary (ie. covered by dedicated Q/Q' diagnostics):
  - Transverse spectrum
    - Check on the presence and amplitude of harmonics of the betatron oscillation
  - Fast Tune → measurement of the tunes with all the BPM’s
  - Frequency maps → Variation of (fast) tunes with initial conditions for visual inspection of the non-linearity

---
Terminology: Accuracy & Precision (also ISO 5725)
Good summary: http://en.wikipedia.org/wiki/Accuracy_and_precision
- Accuracy: “[..] closeness of measurements [..] to its actual (true) value”
- Precision (also: reproducibility or repeatability):	“[..] degree to which repeated measurements	under unchanged conditions show the same results.”
- Example: “Target analogy” and the two extreme cases
Resolution: smallest change that produces a response in the measurement
High precision, but low accuracy
High accuracy, but low precision
we need this from the BPMs
obtained through beam-based alignment

---
Operational Robustness I/II
accelerator operation's point-of-view
- Robust (ie. fault tolerant) measurement of orbit & trajectories ↔ measurement insensitive to:
  - Bunch-by-bunch intensities, bunch filling patterns (“all bunches are created equal, but ...”)
  - Beam intensity losses
    - Intensity ramp-up concept (systematics between pilot and high-intensity beam is paramount)
    - may loose part or full beam during injection, … aim at ~ 90% margin
  - Bunch length or shape changes
    - adiabatic damping, hollow-bunches, …
  - one-gain stage per cycle (if possible), or transparent (automated) gain changes
  - Stability of 'gain calibration' (may recalibrate BPMs 1..2 x day, 1 x per shift but not more for nom. operation)
  - Environmental effects: temperature (amplifier, limiter, cables, …)
  - To a lesser extend: actual orbit in machine (mostly centred)

---
Operational Robustness II/II
Assumptions that may simplify BPM acquisition design:
  - Orbit is most critical for high-intensity operation → high peak-voltages/short bunches
  - Orbit is mostly (by design) in the centre of the beam pipe, e.g. < ± 5 mm
    - Should distinguish three ranges: nominal machine operation (±5 mm), studies/commissioning (±30 mm), ultimate range
    - larger offsets may occur during commissioning but rarely required to control orbit precisely above ±15 mm
  - Only orbit & trajectory measurements needed
    - Required bandwidth ~ 1 kHz & ~ 1 MHz (not 50 MHz) → N.B. (ENOB*Bandwidth)b = const
    - bunch-by-bunch or intra-bunch diagnostics is nice to have but not a must (e.g. optics, orbit, … are not b-b-b sensitive) and could be handled by single dedicated device (notable exception, distinction of 1st, 2nd, 3rd injection)
  - Accuracy, Precision & Resolution:
    - accuracy is important for orbit control but precision is often sufficient
      - need reproducibility, beam-based alignment is key to achieve absolute accuracy
      - centre orbit (↔ el. BPM centre) needs to be rock-solid (i.e. < 0.1 mm)
    - resolution important for relative measurements (e.g. optics, injection/extraction steering, ...)

---
BPM Precision vs. Machine Reproducibility
Question at the core:
If (BPM Precision < Machine reproducibility) → use feedbacks
  - N.B. the only scenario where a real-time (within-cycle) FB makes sense
1. If (BPM precision = Machine reproducibility) → average over cycles →cycle-to-cycle feedbacks
2. If (BPM precision > Machine reproducibility) → forget about FB & switch them 'off'
- Experience with slow extraction in SIS18 seem to indicate a fair machine/orbit reproducibility (on the sub-mm level) for regular cycling
  - quantitative estimates would be beneficial

---
U28+ & Proton – BCMS
Bunch Compression & Merging Scheme
color blue {{{hat I}_{ "max" } over {hat I}_{ "min" }} approx 50}
color blue {{{hat I}_{ "max" } over {hat I}_{ "min" }} succsim 10 ... 50}
x 10 (operation margin)
→ factor 500 (w/o LP)
→ factor <100 (w LP)
adiabatic damping:	~ √E = √~4 → 29 GeV/c	≈ 2.5
RF voltage swing:	~√URF= √~ 10→ 200 kV	≈ 4
bunch stacking:	1 … 4 (8)
OP beam loss margin:	~ 10

---
Alternate SIS100 Injection Scheme
M. Kirk et al. (tentative)

FB1+2
BB2
BB1
Inject from SIS-18 into
2 mono-h buckets:
2R
BB1
Time (turns)
FB2
BB2*
FB1 and FB2 suddenly
reappear 1 and 2 RFPs
to the right, respectively:
FB1
FB2
BB2
FB1 and FB2 each
suddenly reappear 2 RFPs
to the right:
FB1
Barrier Bucket cavities:
BB1 (15 kV)
BB2 (15 kV)
Longitudinal Feed-Back cavities:
FB1 (15 kV)
FB2 (15 kV) N.b. TDR 10 kV each.
Option: after this point,
gradually form 8 bunches
with the h=10 CW cavities.
Reduce barrier bucket length#
RF waveform over a
single RF Period (RFP)
R
Kicker rise time
(2R/5)
Direction of change in
RF during merging
* BB2: fast change in phase by 2 RF periods.
# Alternative for preparation of beam into a h=2 bucket for bunch rotation.
[Speaker Notes: Scheme A (above): Each cavity delivers a single „RF period“ per turn, i.e. single bucket length of a single-h bucket. One could speed things up by merging the 2 SIS-18 bunches and the BB bunch simultaneously, with hopefully little cost in beam phase-space dilution. Could involve 1xFB + 1xBB cavites for each BB pulse in the last optional beam process (pre-compression). Could one reduce the effect of p-s dilution and namely energy spread by stochastic cooling of the beam in the beam-accumulating BB, at least for the early stages of this scheme where the intensity might be perhaps low enough? How long must one wait for coherence in gap of this BB to fade away before it beam would be able to be cooled this way? Scheme B (Originally developed for extraction rigidity and possibly better than A): bunch to bucket transfer in pairs, 4 times sequentially; adiabatically debunch into a BB; [and finally longitudinally squeeze BB for subsequent bunch rotation with compressor cavity.] Could be that one must wait so long for merging during scheme A that it is better to do scheme B with just a single merging of the 8 bunches into a barrier bucket. Scheme C: (POSSIBLE?) Could one include the acceleration cavities (h=10, CW) and hence modify the waveform by subraction with the FB and BB cavities? Advantage is you can have your 15 kV instead of the 10 kV from the FB cavities. -------------------------------------------------------------------------------------------------------------------------------------------------- 1) Cycle period of SIS-18 = ca. 370 ms (2.7 Hz as booster) 2) Scheme A: The 2 FB cavities are powered together to provide an effective 20 kV during the merging of the two SIS-18 injected bunches at the start. The second SIS-18 batch to be merged together and then with the beam in the other BB (left) is, however, merged starting with 10 kV peak RF which is shorter than the ideal value of 15 kV. We therefore should expect some level of p-s dilution as the bunches injected from SIS-18 cannot be matched to the RF bucket contours. Do we expect to perform slow extraction with a gap in beam for the emergency kicker‘s rise time?]

---
Operational Robustness
- FAIR beam parameters vary widely for different species but also within a given cycle setup (e.g. p-bar chain in SIS100):
- BPMs need to be able to cope with:
  - > 10 x bunch length variations
    - adiabatic damping:	~√E	= √~4 → 29 GeV/c	≈ 2.5
    - RF voltage swing:	~√URF	= √~ 10→ 200 kV	≈ 4
    - transition crossing
  - ~ 4 peak signal change (bunch merging/compression scheme)
  - > 90% beam intensity loss during any given cycle
    - dynamic vacuum, UNILAC variations, …
    - also bunch-by-bunch
  - Insensitive to bunch-by-bunch/filling pattern
    - Having a high lower-cut-off frequency is good in this respect
    - Also simplifies base-line restitution
  - typical BPM spec: 30-40 dB instantaneous dynamic range (cable reflections are the limit)

---
SIS18/SIS100 Closed Orbit & Trajectory Control Tolerances – DRAFT
precision
			|Δx|max [σr.m.s.]	|Δx|max [mm]	Ref
CO1	Aperture constraints	mechanical aperture vs. ± n·'beam size'	< 0.5	4	tbc.
CO2	Local orbit at critical points	Collimators hierarchy: local vs. global aperture	1...1/3?		tbc.
CO3		Septa (slow-extraction)	1/3...1/10	??	tbc.
CO3		other aperture constraints		??	tbc.
CO4	Feed-down minimisation	'ΔQ < 0.001' (slow-extraction) / dynamic aperture		1??	tbc.
CO5	Active Systems	centring orbit in RF cavities: minimising field transients & synchro-betatron resonances / TFS/Schottky: improves gain/bandwidth / Interlock BPMs: improves reliability/safety	min.	0.2	tbc.
TR1	Emittance preservation	Injection/extraction mismatch target: / 'Δε/ε < 10%' trans. emittance blow-up / 'Δp/p < 10-3' long. emittance blow-up	1/5	1 … 0.2	X
TR2	Optics Measurement	Beta-beat via phase-advance measurement (relative measurement ↔ resolution)		<0.1 … 0.2 & / σ(φ) < 0.3°	X
TR3	extr. channel acceptance	aperture constraints		4
TR4		collimators		??
TR5		fixed target (e.g. p-Target)/machine interfaces		0.25	X
N.B.SIS100-protons inj: σx,y ≈ 7.7, 3.6 mm extr: σx,y ≈ 3.1, 1.8 mm (@ β = 18 m)

---
Trajectory/Orbit Acquisitions I/II
SIS100 Cycle Example

---
Trajectory/Orbit Acquisitions II/II
Expected FESA Data Streams (Concentrator)
Following modes of acquisition would be expected to be served simultaneously (though some of them could be implemented as down-sampled copies of the higher bandwidth acquisition):
1. Slow-acquisition (FESA property: e.g. 'Orbit'):
  1. Cycle-based acquisition: SIS100 typ. 100 Hz for Archiving System (1k Hz for OP/MDs) → complete trace as a function of time at the end of the cycle
  2. Continuous real-time data publication during the cycle: typ. update rates are around 10-25 Hz for user-level applications or software-based real-time feedbacks
  3. Individual samples at specified times in the cycle: → software interlock on orbit deviations
2. Fast turn-by-turn acquisition (FESA property: e.g. 'Trajectory'):
  1. average batch trajectories in HEBT/HEST (possibly different device)
  2. First 1000 turns for 1st, 2nd, … nth injection
    1. Default & 1st injection: average batch position
    2. ≥ 2nd inj.: gated turn signal on newly injected batch
  3. Last 3 turns → injection/extraction steering
  4. 1..3 study buffers with 10... 100 k turns (to be discussed)
    1. data should be retained for one sequence and can be overwritten in subsequent sequences
    2. event time window may overlap with above reduced acquisition (e.g. BCMS & last turn).
3. Post-Mortem (FESA property 'PostMortem'): not finalized yet but provisionally, it can be foreseen that:
  1. first circular buffer storing the orbit @ 1 kHz for the last second of beam or full cycle
  2. second circular buffer storing the last 1k (10k?) turns.

---
BPM SW Requirements I/II
- All BPM data available from one single source/concentrator
- Expect two separate FESA properties: Orbit & Trajectory
  - N.B. 'Orbit' and 'Trajectory' assumed to be based on turn averages (ie. no bunch-by-bunch → other property for optics control & MD purposes)
- Expected 'Orbit' & 'Trajectory' information (e.g. 2D arrays: BPM index, time):
  1. Average position: x(ti)=[x0(ti), x1(ti), …, xi(ti)]T
    - Orbit: fixed 1 kHz rate or user-defined time stamps (adaptive rate)
    - Trajectory: always first turn (injection), last turn (extraction), + user defined timing events
  1. Measurement noise/error: σ(ti)=[σ0(ti), σ1(ti), …, σi(ti)]T
    - Error propagation of actual averaging variance and known HW noise (e.g. ADC, amplifier)
  1. Relative (qualitative) sum signal Σ = [-1, +1] w.r.t. ADC range
    - allows: cross-checks of ADC range w.r.t. amplifier gain & relative loss localisation
  - BPM statuses (32/64 bit mask)
    - de-selection masks (BI expert, OP), ADC status, timing errors, bunch detection errors, temperature control, range checks, transient errors, etc.

---
BPM SW Requirements II/II
- SIS18/100 - one-to-one mapping: Quads↔ CODs↔ BPMs
  - no singularities by design – good
  - But no redundancy: any missing BPM/COD may cause bump in that region
  - for details see later SVD analysis
- BPM targeted data transfer performance
  - Latency: a priori less of an issue for cycle-to-cycle feedbacks
    - Assumption: data can be read out within ~ 1 s → to be verified
    - Orbit sampling (SIS100) at e.g.:
      - ts= 10 ms (100 Hz)	→ 100 orbits/cycle (1s)	→	< 2.7 kByte/s – non issue
      - ts= 5 ms (200 Hz)	→ 200 orbits/cycle (1s)	→	< 0.5 MByte/s – OK
      - ts= 1 ms (1 kHz)	→ 1000 orbits/cycle (1s)	→	~ 2.6 Mbyte/s – bit more challenging but possible
    - Need to see whether we need constant sampling or whether we can increase/decrease sampling in relation to e.g. the ramp rate, optics changes, slow-extraxtion start etc.
- N.B. need to check whether 'LSA trim' supports these speed and latencies

---
SIS100 BPMs: Input to Archiving
Assumption:
Single Concentrator handling (/republishing) 84 BPMs @ 100 Hz → 3.3 MB/s
N.B. Raw BPM Concentrator Data Rate ~ 32 MB/s (Orbit @ 1 kHz, 10 x 1.5k turn Acq/s)

---
Tentative List of Known Users/Use-Cases
1. Cycle-to-Cycle Feedbacks:
  1. Injection Steering <orbit & trajectory>
  2. Extraction Steering <orbit & trajectory>
  3. SW Orbit-FB during ramp (& Radial-Loop) <orbit only>
2. Archiving System
  1. Regular/OP Archiving <orbit & trajectory>
  2. Post-Mortem System <primarily trajectory>
3. Software Interlock System <orbit & trajectory>
4. Optics Measurement
  1. LOCO-based <primarily orbit & trajectory>
  2. Optics via phase-advance <primarily trajectory>
5. Machine Specific Clients
  1. Multi-Turn Injection Optimisation (SIS18) <orbit & trajectory (1-10k)>
  2. Collimator/Cleaning set-up (SIS100) <orbit>
  3. MPS validation (SIS100) <orbit & trajectory>
  4. Luminosity Steering (HESR) <orbit & trajectory>
6. Machine-Development – all of the above and beyond <orbit & trajectory>
7. ...

---
SIS100 Eigenvector-Matrices
SIS100 Eigenvalue Spectrum
- Eigenvector matrices:
  - U (left) – orthogonal basis for BPMs
  - V (left) – orthogonal basis for CODS
- To note:
  - higher eigenvalues → more local corrections
  - six-fold symmetry visible
|V|

---
SIS100
Full Inverse COD→BPM Response Matrix
N.B. near singularity around extraction (ie. Correction sensitive to BPM noise)
COD

---
Required pbar-Target Position Stability
Asymmetric Beams
Gaussian distribution
εr.m.s. := 1/4εKV
KV-distribution
target
Convolution:
Beam profile
•
Target
N.B. <0.2% of
particles outside
Red = 100%
interaction with target
Blue: 95%
interaction with target
1 mm
0.7 mm

---
Required pbar-Target Position Stability
Round Beams (e.g. via skew-quads in SIS18)
- Gain: ~ 0.1 mm in H for round beams → ± 0.8 mm peak-to-peak variations allowed
- Goal: achieve 95% transmission for 99% of all shots → position control < ~ 250 um
  - Present BPM performance has about 1 mm resolution → needs to be improved (e.g. using hybrids & LP filter)

---
SIS18/SIS100 Slow Extraction I/II
Experiences from ELSA (N.B. e-Machine)
- Slow-Extraction dependence on
  - circulating beam orbit ↔ septa position
  - Feed-down in sextupoles → change of ΔQ & Δβ/β
- Qualitative results from ELSA (hor. emittance ~ step width/efficiency):
a_{"fix"} prop { Q-Q_{"res"} } over { g }
circulating beam orbit-septa separation
courtesy S. Zander, ELSA, IPAC'11
ELSA: gextr ~ 2.5 … 5.5 m-3
may consider checking this quantitatively also for SIS18/100 parameters

---
SIS18/SIS100 Slow Extraction II/II
Experiences from ELSA (N.B. e-Machine)
- Dependence on chromaticity & sextupole strength
  - emittance becomes larger near resonance
courtesy S. Zander, ELSA, IPAC'11

---
Beta-Beat/LHC BPM Prototype System in the SPS-LSS5
βv≈100 m
βv≈100 m
βv≈100 m
βv≈20 m
βv≈100 m
βv≈100 m
Measurement (markers), sinusoidal fit (solid line):
BPMB.513
BPMB.515
BPMB.517
BPMB.518
BPMB.519
BPMB.520
{%DELTA %beta_1} over {%beta_1} ~=~ {cot (%DELTA%mu_{12}^{meas.}) `-` cot (%DELTA%mu_{13}^{meas.})} over {cot (%DELTA%mu_{12}^{theo.}) `-` cot (%DELTA%mu_{13}^{theo.})}
{%DELTA %beta_2} over {%beta_2} ~=~ {cot (%DELTA%mu_{12}^{meas.}) `-` cot (%DELTA%mu_{23}^{meas.})} over {cot (%DELTA%mu_{12}^{theo.}) `-` cot (%DELTA%mu_{23}^{theo.})}
{%DELTA %beta_3} over {%beta_3} ~=~ {cot (%DELTA%mu_{23}^{meas.}) `-` cot (%DELTA%mu_{13}^{meas.})} over {cot (%DELTA%mu_{23}^{theo.}) `-` cot (%DELTA%mu_{13}^{theo.})}
1P.Castro, Luminosity and Betatron Function Measurement at [..] LEP, CERN SL/96-70 (BI)
BPMB.517
BPMB.518
BPMB.519
Δμ12
Δμ13
beam
Δμ ≈ 90°
Δμ ≈ 90°
Δμ≈45°
Δμ≈45°
Δμ≈45°

---
Beta-Beat Measurement Sensitivity
Residual resolution/systematic error
  - 45° optics: requires error below ~1°
  - 89° optics: requires error below ~0.02°
- Statistical noise adds vectorial to the carrier signal:
  - excitation amplitude (carrier signal):	A
  - noise in time (frequency) domain:	σt (σf)
  - Equivalent number of turns:	N
89° optic
{%DELTA %beta_1} over {%beta_1} ~=~ {cot (%DELTA%mu_{12}^{meas.}) `-` cot (%DELTA%mu_{13}^{meas.})} over {cot (%DELTA%mu_{12}^{theo.}) `-` cot (%DELTA%mu_{13}^{theo.})}
45° optic
%DELTA%mu_{1i}^{meas.} := %DELTA%mu_{1i}^{theo.} + %DELTA%varphi_{1i}
70° optic
Best case BPM+kick:
S/N=1mm/0.2mm & 1024 turns
matrix{ %sigma(%varphi) # %=% # alignl { arcsin left({%sigma_{f} over A}right)} # %=% # alignl {arcsin left(sqrt{2 over N}{%sigma_{t} over A}right)} ## % # % % approx % # alignl {sqrt{2 over N}{%sigma_{t} over A}} # % # % }
best case cont.β-Beat
(BBQ-like)
for small noise
to signal ratios
Δβ/β ≈1-2% target

---
Example: LHC Beta-Beat during the Energy Ramp I/II
– Reconstructed Local Beta-Beat
- Excellent fill-to-fill reproducibility of about 1% – provided machine underwent a standard magnetic pre-cycle and no quenches have occurred.
- Complemented also by Rogelio's reproducibility assessment

---
Example: LHC Beta-Beat during the Energy Ramp II/II
– Evolution during a “less-perfect” Ramp
- 3/8 main dipole circuits being pre-cycled to 2 kA instead of the default 6 kA.
- Percent-level correction of the transfer function of one of the warm quadrupole magnet in the vicinity of the test setup
Still, small compared to required dynamic beta-beat of Δβ/β|max< 20%

---
Appendix

---
LHC BPM Specification
LHC-BPM-ES-0004 rev. 2.0, EDMS #327557, 2002, p. 25:
Beam threading
Close trajectory on itself
Position error at injection
Momentum mismatch
detection at injection
Optics and local Q' checks
Aperture optimisations
LHC Collimation/Orbit FB
Orbit at injection elements
Position error at injection
Momentum FB (radial loop)
Dispersion measurements
b2/a2 to b4/a4 (~TOTEM)
Are we happy with this type of format? Other constraints? Open...?

---
BPM System Design & pres. Specifications (f-ds-bd-22e_pos_bpm_1s_v1.0a)
- Accuracy: < 1 mm
  - With k-modulation < 0.2 mm
    - limited to few BPMs at beginning/end of arcs (~12 (24?) out of 84 BPMs)
  - Need other alternatives → RF commutation switches
- Resolution
  - Orbit: ~ 0.1 mm @ 1 kHz
    - OK w.r.t. keeping Δx(s) < 1mm
    - N.B. incompatible with Fast-OFB → possible emittance blow-up
  - Trajectory/turn-by-turn resolution: ~ 1mm
    - Insufficient for target steering & optics measurement → should aim at 0.1 (0.2) mm
%sigma_{orbit@1kHz} approx {1 over {sqrt{n_turns} }} underbrace {color blue {~approx 17}} cdot %sigma_{single-shot@278kHz}
- um-level orbit resolution is not a requirement but a consequence of required turn-by-turn resolution in the order of 100-200 um
  - K.O. exciter as A.C. dipole can produce oscillation amplitudes in the order of 100 um ↔ 500 um → need S/N of ideally > 5/1 → turn-by-turn resolution of ~100 um
Robustness? Why are RF hybrids & LPF/BPF omitted for SIS18 & SIS100 BPMs? Review?
↔ N.B. other (very) similar machines at BNL (AGS) & CERN (PS, PSB, SPS) use them for a good reason.

---
B) Observability – Operational Robustness
– Limits of Direct Sampling & ENOB
Presently proposed SIS18/100 BPM system seem to have issues already for nominal beams and certainly will fail for 'normal' non-ideal beam scenarios encountered during beam commissioning and setup:
- ADC with 12 ENOB & 150 MHz
  - need best performance for high-intensity beams (ie. p & U28+ beams)
  - 50 ns bunch length (2σ) → 8 samples average	→ S/N + 1.5 bit
- SIS100 orbit mostly centred (|Δx| < 5 mm, R≈68 mm):
  - only 2% of the total signal contains the orbit information
  - 98% wasted for intensity/shape information	→ S/N - 6.3 ENOB
- Orbit measurement needs to be most robust not only for nominal operation but even more when things are “bad”:
  - Have to allow for 90-97% losses during cycle	→ S/N - 5.0 ENOB
    - Unexpected UNILAC/SIS18 problems, dynamic vacuum, instabilities
- Nominal bunch length/shape changes	→ S/N - 3.3 ENOB
  - adiabatic damping (Δσ/σ|max ≈ 4), bunch gymnastics (compression, merging, splitting, rotation), transition, hollow-beam, + trigger issues

---
Limits of
Direct Time-Domain Digitization
1990
2000
present
SIS100
closed-orbit
SIS100
turn-by-turn
SIS100
head-tail

---
Proposal
- BPM-ECR: deploy RF hybrid, low-pass filter & RF commutation switches
  - Improve what is important: reliability/robustness of orbit & trajectory measurement
    - ie. don't need 83 'Head-Tail Monitors' that can also measure the orbit/trajectory
    - Ensure function under non-ideal conditions, setup, and commissioning (the “bad days”)
  - Modification proposals:
    - RF hybrid: improves resolution but also accuracy for the mostly centred beams
      - robust centre determination (passive device: insensitive to signal level, power, radiation, gains, ...)
      - Implies ECR for decoupling amplifier gains for individual channels
      - Improved turn-by-turn resolution → enables optics measurement & control
      - Minimises the need for higher-amplitude and multiple kick-per-cycle Q-kicker
    - Low-pass filters:
      - minimise the bunch length & shape dependency
      - but also: improves more robust bunch trigger (more samples/bunch)
    - k-modulation not viable for all SIS100 BPMs to establish 1 mm accuracy target
      - RF commutation switches in front of RF-Hybrid would enable alternate solution
- Deploy 2 (+1) BPMs for the TFS System
  - Permit future vector-sum operation & redundancy for optimal optics
  - additional pick-up for Q/Q' & Head-Tail diagnostics
  - is diode-based base-band-tune (BBQ) Q/Q' technique considered base-line for SIS18/SIS100 operation? Integration?

---
BPM HW – Rationale
- A priori, present electro-static (round) shoe-box-type BPM design is done well
  - PRO:
    - Gives more signal for very low intensity/long bunches
    - very low cut-off frequency ↔ better bunch shape measurement
      - e.g. easier head-tail or bunch length diagnostics
    - Linear by design (other pickups: linear by calibration)
  - CON:
    - too much signal for nominal beams: proton (> 1 kV), U28+ SR (14 V), U28+ FT & U92+
      - Need to be attenuated (N.B. noise figure)
    - bunch filling pattern dependency ↔ more elaborate base-line restitution needed
    - High-impedance operation & collection of static charges (↔ dynamic vacuum, beam losses)
    - impact on longitudinal/transverse impedance
    - much higher complexity/costs compared to simple button-type BPMs
- Question/Gretchen Frage
  - are ultra-low bunch intensities a requirement for SIS100 (e.g. U28+, < 108...109 ppb, > 100 ns r.m.s.)
    - other options exist (e.g. higher RF voltage, slow-extraction, high-low bunch intensity schemes, etc.)
  - what is the lowest bunch intensity/longest bunch length that should be accelerated and diagnosed in the machine
- Probably should stick with the present design but should document (numbers) design choices and decisions

---
Main BPM System Users
- Archiving
  - Quantitative post-operation analysis of machine performance
    - trending, stability
- Post-Mortem
  - mostly on-demand (push) publication in the event of quench/PM trigger
- Operation
  - Initial threading, multi-turn optimisation (SIS18) – on demand
  - Monitoring in MCR
  - cycle-to-cycle injection/extraction steering/feedback – continuous process
    - relies on trajectory data
  - Cycle-to-cycle orbit feedback – continuous process
- Machine Studies/Accelerator Physics – mostly on-demand (but also during OP periods)
  - Linear local/global optics measurement
  - Non-linear optics measurments
- Controls/Machine Protection:
  - Intensity ramp-up & slow software interlocks
    - measured vs. reference orbit comparison on cycle-to-cycle basis
  - to be discussed: in-cycle orbit checks → fast-beam-abort-system